## Slide 1: Vehicular Communication Simulations with NS-3
Konstantinos Katsaros

## Slide 2: Expected outcomes from training
Learn how to write a scenario for vehicular communication evaluation
Learn how to configure your scenario for different environments
Learn about selected topics in more detail
Answer your questions

## Slide 3: Agenda
Basic components of vehicular scenario
Setting up
  Mobility
  Network devices
  Addressing / Routing
  Applications
Getting Results
Integrated Simulators (NS-3 + …)
Q & A

## Slide 4: Vehicular Communications Overview
Figure 1: Vehicular Communications

## Slide 5: Basic Vehicular Scenario Components
Nodes & Mobility
  Vehicles (moving), Road Side Units / Traffic Lights (static), Other (static, moving)
Network Devices
  WiFi (ad-hoc, infrastructure), WAVE, LTE, Wired P2P, Other
Network / Routing
  IPv4/6, Broadcast, MANET/VANET routing protocols, clustering
Applications
  ITS-specific (BSM), Generic On/Off, Ping etc
Figure 2: High-level node architecture

## Slide 6: Nodes & mobility
Where to place the nodes? How do they move?

## Slide 7: Nodes & Mobility
ALL nodes have to be created before simulation starts
Position Allocators setup initial position of nodes
  List, Grid, Random position…
Mobility models specify how nodes will move
  Constant position, constant velocity/acceleration, waypoint…
  Trace-file based from mobility tools such as SUMO, BonnMotion (using NS2 format)
  Routes Mobility using Google API (*)
(*) To be presented in WNS3 - 2015

## Slide 8: Position Allocation Example
  List MobilityHelper mobility; // place two nodes at specific positions (100,0) and (0,100) Ptr<ListPositionAllocator> positionAlloc = CreateObject<ListPositionAllocator> (); positionAlloc->Add (Vector (100, 0, 0)); positionAlloc->Add (Vector (0, 100, 0)); mobility.SetPositionAllocator(positionAlloc);
Grid Position
  MobilityHelper mobility;
  // setup the grid itself: nodes are laid out started from (-100,-100) with 20 per row, the x
  // interval between each object is 5 meters and the y interval between each object is 20 meters
  mobility.SetPositionAllocator ("ns3::GridPositionAllocator",
  "MinX", DoubleValue (-100.0),
  "MinY", DoubleValue (-100.0),
  "DeltaX", DoubleValue (5.0),
  "DeltaY", DoubleValue (20.0),
  "GridWidth", UintegerValue (20),
  "LayoutType", StringValue ("RowFirst"));
Random Rectangle Position
  // place nodes uniformly on a straight line from (0, 1000)
  MobilityHelper mobility;
  Ptr<RandomRectanglePositionAllocator> positionAloc = CreateObject<RandomRectanglePositionAllocator>();
  positionAloc->SetAttribute("X", StringValue("ns3::UniformRandomVariable[Min=0.0|Max=100.0]"));
  positionAloc->SetAttribute("Y", StringValue("ns3::ConstantRandomVariable[Constant=50.0]"));
  mobility.SetPositionAllocator(positionAloc);
Parking lot
Highway road
RSUs/ TL

## Slide 9: Mobility Model Example
Constant Position
  MobilityHelper mobility;
  mobility.SetMobilityModel ("ns3::ConstantPositionMobilityModel");
  mobility.Install (nodes);
Constant Speed
  MobilityHelper mobility;
  mobility.SetMobilityModel ("ns3::ConstantVelocityMobilityModel");
  mobility.Install (nodes);
  Ptr<UniformRandomVariable> rvar = CreateObject<UniformRandomVariable>();
  for (NodeContainer::Iterator i = nodes.Begin (); i != nodes.End (); ++i){
  Ptr<Node> node = (*i);
  double speed = rvar->GetValue(15, 25);
  node->GetObject<ConstantVelocityMobilityModel>()->SetVelocity(Vector(speed,0,0));
  }
Trace-file based
  std::string traceFile = “mobility_trace.txt”;
  // Create Ns2MobilityHelper with the specified trace log file as parameter
  Ns2MobilityHelper ns2 = Ns2MobilityHelper (traceFile);
  ns2.Install (); // configure movements for each node, while reading trace file
Notes: Explain key differences of these models and under what situations would I use each one.

## Slide 10: Interesting ns-3 extensions
ns-3-highway-mobility (https://code.google.com/p/ns-3-highway-mobility/)
  Implement IDM and MOBIL change lane, highway class, traffic-lights.
  Based on ns-3.8
  No longer maintained
Virtual Traffic Lights (PROMELA) (https://dsn.tm.kit.edu/misc_3434.php)
  Manhattan IDM mobility model
  NLOS propagation loss models
  (Virtual) Traffic Light applications

## Slide 11: Hands-on Example (1)
Example training-mobility-example.cc
Scenarios selection
  1. Parking Lot (Static Grid)
  2. Highway (Constant speed)
  3. Urban (Manhattan Grid trace file)

## Slide 12: Network Devices
How nodes communicate? Wireless communication examples.

## Slide 13: Network Devices - WiFi
WiFi module features
  DCF implementation (Basic + RTS/CTS)
  802.11 a/b/g/n (2.4 & 5 GHz) PHY
  MSDU/MPDU aggregation
  QoS support (EDCA only)
  Infrastructure and ad-hoc modes
  Rate adaptation algorithms
More on ns-3 documentation http://www.nsnam.org/docs/models/html/wifi.html

## Slide 14: WiFi Module Architecture

## Slide 15: MAC High
Presently, three MAC high models
  AdhocWifiMac: simplest one
  ApWifiMac: beacon, associations by STAs
  StaWifiMac: association based on beacons
All inherit from RegularWifiMac, which handles QoS and non-QoS support

## Slide 16: MAC Low
MacLow
  RTS/CTS/DATA/ACK transactions
DcfManager
  implements the DCF
DcaTxop and EdcaTxopN:
  One for NonQoS, the other for QoS
  Packet queue
  Fragmentation/Retransmissions

## Slide 17: Rate Control Algorithms
The following rate control algorithms can be used by the MAC low layer:
Algorithms found in real devices:
  ArfWifiManager (default for WifiHelper), OnoeWifiManager, ConstantRateWifiManager, MinstrelWifiManager
Algorithms in literature:
  IdealWifiManager, AarfWifiManager, AmrrWifiManager, CaraWifiManager, RraaWifiManager, AarfcdWifiManager, ParfWifiManager, AparfWifiManager
Example use of constant rate
std::string phyMode ("OfdmRate54Mbps");
wifi.SetRemoteStationManager ("ns3::ConstantRateWifiManager",
"DataMode",StringValue (phyMode),
"ControlMode",StringValue (phyMode));
Other rate managers may not require manual setting as they automatically select the “best” rate

## Slide 18: WiFi PHY
Work at packet (frame) level
Different models available
  YansWifiPhy – default & most widely used
  PhySimWifi (*) – symbol-level, too slow for practical use
  SpectrumWifiPhy (unfinished model, work stalled)
    Models power spectral density of each transmission
    Supports inter-technology interference
Some details are not implemented (e.g. preamble/capture effect)
(*) https://dsn.tm.kit.edu/english/ns3-physim.php

## Slide 19: Propagation Models
Propagation Loss
  ITUR1411, LogDistance, ThreeLogDistance, Range, TwoRayGround, Friis
  Nakagami, Jakes
  Obstacle model (*)
Propagation Delay
  Constant Speed
  Random
Be careful when using YansWifiChannelHelper::Default() the LogDistance propagation model is added. Calling AddPropagationLoss() again will add a second propagation loss model.
(*) To be presented in WNS3 2015

## Slide 20: Communication Range
Depends on many factors
  Propagation loss model and PHY configuration
  Frame size (big vs small)
  Transmission mode (6Mbps vs 54 Mbps)

## Slide 21: Hands-on Example (2)
Example training-wifi-example.cc
Scenarios
  Adhoc, Infrastructure
  IEEE 802.11a/b/g
  QoS/Non-QoS

## Slide 22: Network Devices - WAVE
WAVE features:
  MAC layer (IEEE 802.11p) – “Outside the context of a BSS (OCB)”
  Multi-channel operation (IEEE 1609.4)
  Management information through vendor specific action (VSA) frame.
More on ns-3 documentation http://www.nsnam.org/docs/models/html/wave.html
Notes: This MAC does not require any association between devices (similar to an adhoc WiFi MAC)

## Slide 23: WAVE Module Architecture
WaveNetDevice
IEEE 1609.4
OcbWifiMac
SchChannelScheduler, ChannelManager, VSARepeater, ChannelCoortinator
Send, SendWsmp, SendVsa
ForwardUp,
ForwardVsa
WAVE
module
WIFI
module

## Slide 24: WAVE Module Design (1)
WaveNetDevice
  has multiple internal MAC entities, each one used to support each channel.
  allows for multiple PHY entities, permitting single/multiple-PHY.
OcbWifiMac
  similar to AdhocWifiMac
SendX
  sends a WSMP packets, specifying Tx parameters, e.g. channel number.
Send/SetReceiveCallback
  allows the sending all IP-based packets.

## Slide 25: Multi-channel Operations (IEEE 1609.4 - 2013)
Continuous
(b) Alternating
(c) Immediate
(d) Extended
Channel 178 is the control channel (CCH).
Channels 172, 174, 176, 180, 182, and 184 are service channels (SCH).
Channels 174 and 176 and channels 180 and 182 could be combined to produce two twenty megahertz channels, channels 175 and 181, respectively.

## Slide 26: WAVE Module Design (2)
ChannelScheduler
  provides API to switch channels. Current implementation: DefaultChannelScheduler multi-channel, single PHY. StartSch/StopSch assigns channel access for sending packets.
  used to assign access for ContinuousAccess, ExtendedAccess, AlternationgAccess
ChannelCoordinator
  used to generate channel coordination events. Current default channel intervals are: 50ms CCH, 50ms SCH, 4ms Guard.
Register/DeleteTxProfile
  should be registered to specify tx parameters before transmission.

## Slide 27: Channel Access Assignment
Continuous (Default)
  for (uint32_t i = 0; i != devices.GetN (); ++i){
  Ptr<WaveNetDevice> device = DynamicCast<WaveNetDevice>(devices.Get(i));
  // Alternating access without immediate channel switch
  const SchInfo schInfo = SchInfo (SCH1, true, EXTENDED_CONTINUOUS);
  Simulator::Schedule (Seconds (0.0), &WaveNetDevice::StartSch, device, schInfo);
  }
Alternating
  Configure channel intervals. Default 50/50ms.
  Config::SetDefault ("ns3::ChannelCoordinator::CchInterval", TimeValue (MilliSeconds(80)));
  Config::SetDefault ("ns3::ChannelCoordinator::SchInterval", TimeValue (MilliSeconds(20)));
  for (uint32_t i = 0; i != devices.GetN (); ++i){
  Ptr<WaveNetDevice> device = DynamicCast<WaveNetDevice>(devices.Get(i));
  // Alternating access without immediate channel switch
  const SchInfo schInfo = SchInfo (SCH1, false, EXTENDED_ALTERNATING);
  Simulator::Schedule (Seconds (0.0), &WaveNetDevice::StartSch, device, schInfo);
  }
Extended
  for (uint32_t i = 0; i != devices.GetN (); ++i){
  Ptr<WaveNetDevice> device = DynamicCast<WaveNetDevice>(devices.Get(i));
  // Extended access for 8 SYNC intervals without immediate channel switch
  const SchInfo schInfo = = SchInfo (SCH1, false, 8);
  Simulator::Schedule (Seconds (0.0), &WaveNetDevice::StartSch, device, schInfo);
  }
Tx Profile
  the IP-based packets will be transmitted in SCH1 with 6Mbps and 4 txPowerLevel with adaptable mode.
  const TxProfile txProfile = TxProfile (SCH1, true, 4, WifiMode("OfdmRate6MbpsBW10MHz"));
  Simulator::Schedule (Seconds (2.0), &WaveNetDevice::RegisterTxProfile, sender, txProfile);
Notes: I recently learned that US Stds expect there to be NO time coordination, and that (dedicated, continuous) channel access is completely random.

## Slide 28: Hands-on Example (3)
Examples wave-simple-802.11p.cc & wave-simple-device.cc
  IEEE 802.11p example
  WAVE example for sending WSMP, simple IP, and VSA packets

## Slide 29: Internetworking
How everything is linked? Addressing, routing protocols etc.

## Slide 30: Network (IP / Routing)
IPv4 and IPv6 addressing available, but restrictions in routing implementations
Ad-hoc routing protocols (IPv4 only)
  AODV, OLSR, DSR, DSDV
  GPSR, CLWPR (*)
  Epidemic (**)
  Cluster (**)
Different setup (see manet/vanet-routing-compare.cc)
Some are sensitive to start time.
Also possible:
  Use linux-kernel implementation with DCE, e.g. NEMO, MIP.
  Calculate routes offline and use static routes.
(*) Presented in WNS3 2012
(**) To be presented in WNS3 2015

## Slide 31: Applications
ITS specific
  BSMApplication: Broadcast Basic Safety Messages periodically.
    Dummy packets 200bytes @ 10Hz only if node is moving
    WaveBsmStats used to manage statistics
Generic (sample)
  OnOffApplication: Generate traffic with constant bit rate during the ON period.
    Control data rate, packet size, On/Off times
  Ping: send ICMP ECHO requests and wait for reply
    Control packet size, interval

## Slide 32: Setting Up Applications
Timing is very important in wireless simulations
Setting multiple applications to start at the same time is not a good idea in general (ApplicationContainer::Start () sets all in container)
Nodes are likely to initiate route building process at the exact same time
  collision is almost guaranteed

## Slide 33: Maximum “Application” Rate
The maximum achievable “application” data rate is not the same as the “Wi-Fi” rate due to:
  Timing (IFS)
  RTS/CTS/ACK
  Multihop (shared medium)
Avoid setting application rate == Wi-Fi rate

## Slide 34: QoS support
Use of QosTag to mark packets with higher priority for use by QoS-aware MAC
void
TagMarker(Ptr<const Packet> packet)
{
QosTag qosTag;
qosTag.SetUserPriority(UP_VO);
packet->AddPacketTag (qosTag);
}
Config::ConnectWithoutContext ("/NodeList/*/ApplicationList/*/$ns3::OnOffApplication/Tx", MakeCallback (&TagMarker));

## Slide 35: Getting Results
FlowMonitor
  Only unicast IP flows (over TCP/UDP).
  Known issues with DSR
ASCII Trace Analyzing
  Slow process, generates large files
Data Collection Framework
  Exploit trace sources to capture events (e.g. packet Tx/Rx) and analyze them during simulation.
  Probe: mechanism to instrument and control output in the form of trace sources.
  Collector: consumes data generated from probes.
  Aggregator: end point of data collection.
  Plot with GnuPlot, save to data bases/files.

## Slide 36: Hands-on Example (4)
Example vanet-routing-compare.cc
Scenarios:
  1. Random Waypoint Mobility, 40 nodes, IEEE 802.11p continuous access
  2. Trace source mobility (Zurich), 99 vehicles
  BSM application and IP traffic with selection of routing protocols (AODV default)

## Slide 37: Hands-on Example (5)
Example training-wave-example.cc
Scenarios
  1. Continuous: continuous access for default CCH channel.
  2. Alternating: alternating access for default 50ms CCHI on CCH channel and default 50ms SCHI on SCH channel.
  3. Alternating-80-20: alternating access for 80ms CCHI on CCH channel and 20ms SCHI on SCH channel.
  4. Alternating-20-80: alternating access for 20ms CCHI on CCH chanel and 80ms SCHI on SCH channel.

## Slide 38: Integrated simulators
Online coupling of NS-3 and mobility simulators
  iTETRIS (http://www.ict-itetris.eu/)
    Coupled with ns-3.18
    Provides complete ETSI ITS stack
  VNS (http://www.dcc.fc.up.pt/~rjf/vns/index.html)
    Based on ns-3.16 (loosely coupled)
  VSimRTI (https://www.dcaiti.tu-berlin.de/research/simulation/)
    Coupled with ns-3.15
  ONVIS (http://ovnis.gforge.uni.lu/)
    Based on ns-3.10

## Slide 39: References & Acknowledgments
Daniel Lertpratchya, “Wi-Fi Module in NS-3”, NS-3 training, 2014
NS-3 documentation https://www.nsnam.org/docs/models/html/index.html
Thanks to Junling Bu and Scott Carpenter for example codes

## Slide 40
Q&A