## Slide 1
ns-3 Training

## Slide 2: Outline
Wi-Fi in detail
  Support of standard features
  Architecture
  Configuration via helpers
Advanced use case: LAA-Wifi-Coexistence
  SpectrumWifiPhy
  Adding a LBT Access Manager
  Scenario support
  Output data processing

## Slide 3: Wi-Fi Overview
WiFi module features
  DCF implementation (Basic + RTS/CTS)
  802.11 a/b/g/n/ac (2.4 & 5 GHz) PHY
  MSDU/MPDU aggregation
  QoS support (EDCA)
  Infrastructure and ad-hoc modes
  Many rate adaptation algorithms
  AWGN-based error models
Unsupported features
  MIMO
  11ac advanced features (Tx beamforming, Mu-MIMO)
Related modules
  Mesh (802.11s) and WAVE (802.11p/vehicular)

## Slide 4: Wi-Fi Architecture

## Slide 5: MAC High
Presently, three MAC high models
  AdhocWifiMac: simplest one
  ApWifiMac: beacon, associations by STAs
  StaWifiMac: association based on beacons
All inherit from RegularWifiMac, which handles QoS and non-QoS support

## Slide 6: Rate controls
The following rate control algorithms can be used by the MAC low layer:
Algorithms found in real devices:
  ArfWifiManager (default for WifiHelper), OnoeWifiManager, ConstantRateWifiManager, MinstrelWifiManager, MinstrelHtWifiManager
Algorithms in literature:
  IdealWifiManager, AarfWifiManager, AmrrWifiManager, CaraWifiManager, RraaWifiManager, AarfcdWifiManager, ParfWifiManager, AparfWifiManager
Example use of constant rate
std::string phyMode ("OfdmRate54Mbps");
wifi.SetRemoteStationManager ("ns3::ConstantRateWifiManager",
"DataMode",StringValue (phyMode),
"ControlMode",StringValue (phyMode));

## Slide 7: MAC Middle/Low
Three components:
MacLow
  RTS/CTS/DATA/ACK transactions
  Aggregation, Block acks
DcfManager
  implements the DCF
DcaTxop and EdcaTxopN:
  One for NQoS, the other for QoS
  Packet queue
  Fragmentation/Retransmissions

## Slide 8: Current Wi-Fi PHY abstraction

## Slide 9: Physical layer
No AGC model
Sync on first RX with energy > detection threshold
Collision: the error model will likely cause a drop of the packet
No capture effect: won’t re-sync on a stronger packet

## Slide 10: Error models
Based on analytical models with error bounds
Three implementations with different bounds: YansErrorRateModel, NistErrorRateModel, DssErrorRateModel
NistErrorRateModel (OFDM)
DsssErrorRateModel

## Slide 11: Interference helper
SINR evaluated on chunk-by-chunk basis

## Slide 12: Configuring 802.11n/ac
Example programs include
  examples/wireless/ht-wifi-network.cc
  examples/wireless/vht-wifi-network.cc
  examples/wireless/wifi-aggregation.cc
Setting the WifiPhyStandard will set most defaults reasonably
  WifiHelper wifi;
  wifi.SetStandard (WIFI_PHY_STANDARD_80211ac);
  WifiMacHelper mac;
802.11ac uses 80 MHz channel by default; 802.11n uses 20 MHz

## Slide 13: 802.11n/ac rate controls
Possible options are IdealWifiManager, MinstrelHtWifiManager, and ConstantRateWifiManager
examples:
  src/wifi/examples/ideal-wifi-manager-example.cc
  src/wifi/examples/minstrel-ht-wifi-manager-example.cc

## Slide 14: Example output for MinstrelHt
$ ./waf --run "minstrel-ht-wifi-manager-example --standard=802.11n-5GHz"
$ gnuplot minstrel-ht-802.11n-5GHz-20MHz-LGI-1SS.plt

## Slide 15: Typical configuration
std::string phyMode ("DsssRate1Mbps");
NodeContainer ap;
ap.Create (1);
NodeContainer sta;
sta.Create (2);
WifiHelper wifi;
wifi.SetStandard (WIFI_PHY_STANDARD_80211b);
YansWifiPhyHelper wifiPhy = YansWifiPhyHelper::Default ();
// ns-3 supports RadioTap and Prism tracing extensions for 802.11
wifiPhy.SetPcapDataLinkType (YansWifiPhyHelper::DLT_IEEE802_11_RADIO);
YansWifiChannelHelper wifiChannel;
// reference loss must be changed since 802.11b is operating at 2.4GHz
wifiChannel.SetPropagationDelay ("ns3::ConstantSpeedPropagationDelayModel");
wifiChannel.AddPropagationLoss ("ns3::LogDistancePropagationLossModel",
"Exponent", DoubleValue (3.0),
"ReferenceLoss", DoubleValue (40.0459));
wifiPhy.SetChannel (wifiChannel.Create ());

## Slide 16: Typical configuration (cont.)
// Add a non-QoS upper mac, and disable rate control
WifiMacHelper wifiMac;
wifi.SetRemoteStationManager ("ns3::ConstantRateWifiManager",
"DataMode",StringValue (phyMode),
"ControlMode",StringValue (phyMode));
// Setup the rest of the upper mac
Ssid ssid = Ssid ("wifi-default");
// setup ap.
wifiMac.SetType ("ns3::ApWifiMac",
"Ssid", SsidValue (ssid));
NetDeviceContainer apDevice = wifi.Install (wifiPhy, wifiMac, ap);
NetDeviceContainer devices = apDevice;
// setup sta.
wifiMac.SetType ("ns3::StaWifiMac",
"Ssid", SsidValue (ssid),
"ActiveProbing", BooleanValue (false));
NetDeviceContainer staDevice = wifi.Install (wifiPhy, wifiMac, sta);
devices.Add (staDevice);

## Slide 17: Typical configuration (cont.)
// Configure mobility
MobilityHelper mobility;
Ptr<ListPositionAllocator> positionAlloc = CreateObject<ListPositionAllocator> ();
positionAlloc->Add (Vector (0.0, 0.0, 0.0));
positionAlloc->Add (Vector (5.0, 0.0, 0.0));
positionAlloc->Add (Vector (0.0, 5.0, 0.0));
mobility.SetPositionAllocator (positionAlloc);
mobility.SetMobilityModel ("ns3::ConstantPositionMobilityModel");
mobility.Install (ap);
mobility.Install (sta);
// other set up (e.g. InternetStack, Application)

## Slide 18: Athstats helper
Hooks Wi-Fi traces to provide debugging similar to Madwifi drivers
Example athstats output from example ./waf --run wifi-ap
m_txCount m_rxCount unused short long exceeded rxError
0 0 0 0 0 0 0 0 0 0 0M
0 60 0 0 0 0 0 0 0 0 0M
0 123 0 0 0 0 0 0 0 0 0M
0 122 0 0 0 0 0 0 0 0 0M
0 122 0 0 0 0 0 0 0 0 0M
0 122 0 0 0 0 0 0 0 0 0M
0 122 0 0 0 0 2 0 0 0 0M
0 122 0 0 0 0 23 0 0 0 0M
0 122 0 0 0 0 14 0 0 0 0M
0 122 0 0 0 0 14 0 0 0 0M
0 122 0 0 0 0 26 0 0 0 0M
0 122 0 0 0 0 12 0 0 0 0M

## Slide 19: LTE/Wi-Fi Coexistence

## Slide 20: Use case: LAA Wi-Fi Coexistence
ns-3 has been extended to support scenarios for LTE LAA/Wi-Fi Coexistence
Methodology defined in 3GPP Technical Report TR36.889
Enhancements needed:
  Wireless models (LBT access manager, SpectrumWifiPhy, propagation/fading models)
  Scenario support (traffic models)
  Output data processing

## Slide 21: Indoor 3GPP scenario

## Slide 22: Indoor scenario details

## Slide 23: Outdoor 3GPP scenario
Outdoor layout: hexagonal macrocell layout. 7 macro sites and 3 cells per site. 1 Cluster per cell. 4 small cells per operator per cluster, uniformly dropped. ITU UMi channel model.
Figure source: 3GPP TR 36.889 V13.0.0 (2015-05)

## Slide 24: References
ns-3 Wiki page:
  https://www.nsnam.org/wiki/LAA-WiFi-Coexistence
    module documentation
    references to various publications
    documentation on reproducing results
Code:
  http://code.nsnam.org/laa/ns-3-lbt

## Slide 25: Sample results

## Slide 26: Wi-Fi enhancements

## Slide 27: Model enhancements: Wi-Fi
Spectrum Wi-Fi Phy implementation
Wi-Fi preamble detection based on AWGN and TGn Channel Model D
Wi-Fi RSS-based AP selection and roaming
Wi-Fi MIMO approximations to support 2x2 DL, 1x2 DL on AWGN and TGn Model D

## Slide 28: Model enhancements: LTE
LTE interference model relies on the simplifying assumption that all interfering signals are LTE and are synchronized at the subframe level.
LTE inteference model has been enhanced to handle inteference by signals of any type.
This relies on the ns-3 Spectrum framework.
The reception of LTE signals is evaluated by chunks, where each chunk is identified by a constant power spectral density.

## Slide 29: Scenario
An initial test scenario, useful for testing basic model operation in a small scale setting, grew into TR36.889-like indoor and outdoor scenarios
D1 and d2 can vary and operator A and B can be both LTE or Wi-Fi

## Slide 30: Output experiment scripts
Shell scripts and gnuplot helpers to manage configuration and data output
(demonstrate)

## Slide 31: Status
Portions are being migrated into ns-3-dev
  SpectrumWifiPhy in ns-3.26
  LTE components, propagation model likely in ns-3.27
  Scenario helper may be rewritten
Trying to decompose into pieces easy to merge
For more information:
  https://www.nsnam.org/wiki/LAA-WiFi-Coexistence