## Slide 1
ns-3 Training

## Slide 2: Example walkthrough
This section progressively builds up a simple ns-3 example, explaining concepts along the way
Files for these programs are available on the ns-3 wiki

## Slide 3: Example program
wns3-version1.cc
  Link found on wiki page
  Place program in scratch/ folder

## Slide 4: Fundamentals
Key objects in the simulator are Nodes, Packets, and Channels
Nodes contain Applications, “stacks”, and NetDevices

## Slide 5: Node basics
A Node is a shell of a computer to which applications, stacks, and NICs are added
Application
Application
Application
“DTN”

## Slide 6: NetDevices and Channels
NetDevices are strongly bound to Channels of a matching type
ns-3 Spectrum models relax this assumption
Nodes are architected for multiple interfaces
WifiNetDevice
WifiChannel

## Slide 7: Internet Stack
Internet Stack
  Provides IPv4 and some IPv6 models currently
No non-IP stacks ns-3 existed until 802.15.4 was introduced in ns-3.20
  but no dependency on IP in the devices, Node object, Packet object, etc. (partly due to the object aggregation system)

## Slide 8: Other basic models in ns-3
Devices
  WiFi, WiMAX, CSMA, Point-to-point, ...
Error models and queues
Applications
  echo servers, traffic generator
Mobility models
Packet routing
  OLSR, AODV, DSR, DSDV, Static, Nix-Vector, Global (link state)

## Slide 9: Structure of an ns-3 program
int main (int argc, char *argv[])
{
// Set default attribute values
// Parse command-line arguments
// Configure the topology; nodes, channels, devices, mobility
// Add (Internet) stack to nodes
// Configure IP addressing and routing
// Add and configure applications
// Configure tracing
// Run simulation
}

## Slide 10: Helper API
The ns-3 “helper API” provides a set of classes and methods that make common operations easier than using the low-level API
Consists of:
  container objects
  helper classes
The helper API is implemented using the low-level API
Users are encouraged to contribute or propose improvements to the ns-3 helper API

## Slide 11: Containers
Containers are part of the ns-3 “helper API”
Containers group similar objects, for convenience
  They are often implemented using C++ std containers
Container objects also are intended to provide more basic (typical) API

## Slide 12: The Helper API (vs. low-level API)
Is not generic
Does not try to allow code reuse
Provides simple 'syntactical sugar' to make simulation scripts look nicer and easier to read for network researchers
Each function applies a single operation on a ''set of same objects”
A typical operation is "Install()"

## Slide 13: Helper Objects
NodeContainer: vector of Ptr<Node>
NetDeviceContainer: vector of Ptr<NetDevice>
InternetStackHelper
WifiHelper
MobilityHelper
OlsrHelper
... Each model provides a helper class

## Slide 14: Installation onto containers
Installing models into containers, and handling containers, is a key API theme
NodeContainer c;
c.Create (numNodes);
...
mobility.Install (c);
...
internet.Install (c);
...

## Slide 15: Native IP models
IPv4 stack with ARP, ICMP, UDP, and TCP
IPv6 with ND, ICMPv6, IPv6 extension headers, TCP, UDP
IPv4 routing: RIPv2, static, global, NixVector, OLSR, AODV, DSR, DSDV
IPv6 routing: RIPng, static

## Slide 16: IP address configuration
An Ipv4 (or Ipv6) address helper can assign addresses to devices in a NetDevice container
Ipv4AddressHelper ipv4;
ipv4.SetBase ("10.1.1.0", "255.255.255.0");
csmaInterfaces = ipv4.Assign (csmaDevices);
...
ipv4.NewNetwork (); // bumps network to 10.1.2.0
otherCsmaInterfaces = ipv4.Assign (otherCsmaDevices);

## Slide 17: Internet stack
The public interface of
the Internet stack is
defined (abstract base
classes) in
src/network/model
directory
The intent is to support
multiple implementations
The default ns-3 Internet
stack is implemented in
src/internet-stack

## Slide 18: ns-3 TCP
Four options exist:
  native ns-3 TCP
  TCP simulation cradle (NSC)
  Direct code execution (Linux/FreeBSD library)
  Use of virtual machines
To enable NSC:
internetStack.SetNscStack ("liblinux2.6.26.so");

## Slide 19: Native TCP models
TCP NewReno is baseline
  TCP SACK under review for ns-3.26
TCP congestion control recently refactored, and many TCP variants are under finalization
  Present: BIC, Highspeed, Hybla, Illinois, Scalable, Vegas, Veno, Westwood, YeAH
  Pending: CUBIC, H-TCP, SACK
MP-TCP is under development from past summer project (for ns-3.27?)

## Slide 20: ns-3 simulation cradle
Port by Florian Westphal of Sam Jansen’s Ph.D. work
Figure reference: S. Jansen, Performance, validation and testing with the Network
Simulation Cradle. MASCOTS 2006.

## Slide 21: ns-3 simulation cradle
For ns-3:
Linux 2.6.18
Linux 2.6.26
Linux 2.6.28
Others:
FreeBSD 5
lwip 1.3
OpenBSD 3
Other simulators:
ns-2
OmNET++
Figure reference: S. Jansen, Performance, validation and testing with the Network
Simulation Cradle. MASCOTS 2006.

## Slide 22: Review of sample program (cont.)
ApplicationContainer apps;
OnOffHelper onoff ("ns3::UdpSocketFactory",
InetSocketAddress ("10.1.2.2", 1025));
onoff.SetAttribute ("OnTime", StringValue ("Constant:1.0"));
onoff.SetAttribute ("OffTime", StringValue ("Constant:0.0"));
apps = onoff.Install (csmaNodes.Get (0));
apps.Start (Seconds (1.0));
apps.Stop (Seconds (4.0));
PacketSinkHelper sink ("ns3::UdpSocketFactory",
InetSocketAddress ("10.1.2.2", 1025));
apps = sink.Install (wifiNodes.Get (1));
apps.Start (Seconds (0.0));
apps.Stop (Seconds (4.0));
Traffic generator
Traffic receiver

## Slide 23: Applications and sockets
In general, applications in ns-3 derive from the ns3::Application base class
  A list of applications is stored in the ns3::Node
  Applications are like processes
Applications make use of a sockets-like API
  Application::Start () may call ns3::Socket::SendMsg() at a lower layer

## Slide 24: Sockets API
Plain C sockets
int sk;
sk = socket(PF_INET, SOCK_DGRAM, 0);
struct sockaddr_in src;
inet_pton(AF_INET,”0.0.0.0”,&src.sin_addr);
src.sin_port = htons(80);
bind(sk, (struct sockaddr *) &src, sizeof(src));
struct sockaddr_in dest;
inet_pton(AF_INET,”10.0.0.1”,&dest.sin_addr);
dest.sin_port = htons(80);
sendto(sk, ”hello”, 6, 0, (struct sockaddr *) &dest, sizeof(dest));
char buf[6];
recv(sk, buf, 6, 0);
}
ns-3 sockets
Ptr<Socket> sk =
udpFactory->CreateSocket ();
sk->Bind (InetSocketAddress (80));
sk->SendTo (InetSocketAddress (Ipv4Address (”10.0.0.1”), 80), Create<Packet> (”hello”, 6));
sk->SetReceiveCallback (MakeCallback (MySocketReceive));
[…] (Simulator::Run ())
void MySocketReceive (Ptr<Socket> sk, Ptr<Packet> packet)
{
...
}

## Slide 25: New in ns-3.25: traffic control
Patterned after Linux traffic control, allows insertion of software-based priority queues between the IP layer and device layer
  pfifo_fast, RED, Adaptive RED, CoDel
  planned for ns-3.26: FQ-CoDel, PIE, Byte Queue Limits (BQL)

## Slide 26: NetDevice trace hooks
Example: CsmaNetDevice
CsmaNetDevice::Send ()
CsmaNetDevice::
TransmitStart()
CsmaNetDevice::
Receive()
CsmaChannel
NetDevice::
ReceiveCallback
queue
MacRx
MacDrop
MacTx
MacTxBackoff
PhyTxBegin
PhyTxEnd
PhyTxDrop
Sniffer
PromiscSniffer
PhyRxEnd
PhyRxDrop

## Slide 27: Nodes, Mobility, and Position
ALL nodes have to be created before simulation starts
Position Allocators setup initial position of nodes
  List, Grid, Random position…
Mobility models specify how nodes will move
  Constant position, constant velocity/acceleration, waypoint…
  Trace-file based from mobility tools such as SUMO, BonnMotion (using NS2 format)
  Routes Mobility using Google API (*)
(*) Presented in WNS3 - 2015

## Slide 28: Position Allocation Examples
  List MobilityHelper mobility; // place two nodes at specific positions (100,0) and (0,100) Ptr<ListPositionAllocator> positionAlloc = CreateObject<ListPositionAllocator> (); positionAlloc->Add (Vector (100, 0, 0)); positionAlloc->Add (Vector (0, 100, 0)); mobility.SetPositionAllocator(positionAlloc);
Grid Position
  MobilityHelper mobility;
  // setup the grid itself: nodes are laid out started from (-100,-100) with 20 per row, the x
  // interval between each object is 5 meters and the y interval between each object is 20 meters
  mobility.SetPositionAllocator ("ns3::GridPositionAllocator",
  "MinX", DoubleValue (-100.0),
  "MinY", DoubleValue (-100.0),
  "DeltaX", DoubleValue (5.0),
  "DeltaY", DoubleValue (20.0),
  "GridWidth", UintegerValue (20),
  "LayoutType", StringValue ("RowFirst"));
Random Rectangle Position
  // place nodes uniformly on a straight line from (0, 1000)
  MobilityHelper mobility;
  Ptr<RandomRectanglePositionAllocator> positionAloc = CreateObject<RandomRectanglePositionAllocator>();
  positionAloc->SetAttribute("X", StringValue("ns3::UniformRandomVariable[Min=0.0|Max=100.0]"));
  positionAloc->SetAttribute("Y", StringValue("ns3::ConstantRandomVariable[Constant=50.0]"));
  mobility.SetPositionAllocator(positionAloc);

## Slide 29: Mobility Model Example
Constant Position
  MobilityHelper mobility;
  mobility.SetMobilityModel ("ns3::ConstantPositionMobilityModel");
  mobility.Install (nodes);
Constant Speed
  MobilityHelper mobility;
  mobility.SetMobilityModel ("ns3::ConstantVelocityMobilityModel");
  mobility.Install (nodes);
  Ptr<UniformRandomVariable> rvar = CreateObject<UniformRandomVariable>();
  for (NodeContainer::Iterator i = nodes.Begin (); i != nodes.End (); ++i){
  Ptr<Node> node = (*i);
  double speed = rvar->GetValue(15, 25);
  node->GetObject<ConstantVelocityMobilityModel>()->SetVelocity(Vector(speed,0,0));
  }
Trace-file based
  std::string traceFile = “mobility_trace.txt”;
  // Create Ns2MobilityHelper with the specified trace log file as parameter
  Ns2MobilityHelper ns2 = Ns2MobilityHelper (traceFile);
  ns2.Install (); // configure movements for each node, while reading trace file
Notes: Explain key differences of these models and under what situations would I use each one.

## Slide 30: Interesting ns-3 extensions
ns-3-highway-mobility (https://code.google.com/p/ns-3-highway-mobility/)
  Implement IDM and MOBIL change lane, highway class, traffic-lights.
  Based on ns-3.8
  No longer maintained
Virtual Traffic Lights (PROMELA) (https://dsn.tm.kit.edu/misc_3434.php)
  Manhattan IDM mobility model
  NLOS propagation loss models
  (Virtual) Traffic Light applications

## Slide 31: Propagation Models
Propagation Loss
  ITUR1411, LogDistance, ThreeLogDistance, Range, TwoRayGround, Friis
  Nakagami, Jakes
  Obstacle model (*)
Propagation Delay
  Constant Speed
  Random
Be careful when using YansWifiChannelHelper::Default() the LogDistance propagation model is added. Calling AddPropagationLoss() again will add a second propagation loss model.
(*) Presented in WNS3 2015

## Slide 32: Communication Range
Depends on many factors
  Propagation loss model and PHY configuration
  Frame size (big vs small)
  Transmission mode (6Mbps vs 54 Mbps)

## Slide 33: Example program iterations
Walk through four additional revisions of the example program
  wns3-version2.cc
  wns3-version3.cc
  wns3-version4.cc