## Slide 1: Tracing in NS-3
DRAFT Version 1
May, 2014
This work was performed under the auspices of the U.S. Department of Energy by Lawrence Livermore National Security, LLC, Lawrence Livermore National Laboratory under Contract DE-AC52-07NA27344.
Walid Younes

## Slide 2: Chapter 7: Tracing
Online tutorial: http://www.nsnam.org/docs/release/3.14/tutorial/singlehtml/index.html#tracing
T. Predojev (2012): http://wikienergy.cttc.es/images/2/2d/Ns-3-tutorial-complete.pdf
M. Lacage (2009): http://www.nsnam.org/tutorials/ns-3-tutorial-tunis-apr09.pdf
G. Riley (2008): http://www.wns2.org/docs/wns_tutorial-handout.pdf
S. Kristiansen (2010): http://www.uio.no/studier/emner/matnat/ifi/INF5090/v11/undervisningsmateriale/INF5090-NS-3-Tutorial-2011-Oslo-slides.pdf
Source material:

## Slide 3: More advanced tracing with NS3
You can use ascii, pcap tracing or logging to get info from your sim
  Need to write code to parse output
  The info you want may not be obtainable by pre-defined mechanisms
There is another way in NS3
  Add your own traces to events you care about
  Produce output in a convenient form
  Add hooks to the core that can be accessed by other users later

## Slide 4: You could use print statements, but I wouldn’t recommend it
You may have to dig deep inside the NS3 core to find the info you want
More print statements ⇒ need way to enable/disable specific ones
  Congratulations! You’ve just re-invented the NS3 logging system!
You could add logging statements to the core
  Remember: NS3 is open-source, evolving system
    Core will bloat to include all possible log messages
    Unwieldy gigantic log files ⇒ effectively useless
    No guarantee specific log messages will survive releases
Logging ≠ Tracing

## Slide 5: The basic idea: trace sources and sinks
You need:
  Trace source: signals sim event and provides access to the data
  Trace sink: consumes the trace info, do something useful with it
  Mechanism to connect trace source to trace sink
Note: there can be many sinks connected to the same trace source
Trace source
Trace sink
Trace sink
Trace sink

## Slide 6: A simple low-level example: callbacks
This is the key to the way tracing works
In C/C++ you can pass a pointer to a function: callback mechanism
Trace source maintains a list of callback functions added by the sinks
When an event of interest happens
  Trace source passes data to the callback functions
  Callback functions are executed
float myFunction(float x)
{
return x*x;
}
⋮
float Integrate(float (*func)(float), float lo, float hi)
{
…
}
⋮
Integrate(&myFunction,0,1);
Ex: a function to integrate functions

## Slide 7: A simple low-level example: fourth.cc
#include "ns3/object.h"
#include "ns3/uinteger.h"
#include "ns3/traced-value.h"
#include "ns3/trace-source-accessor.h"
#include <iostream>
using namespace ns3;
class MyObject : public Object
{
public:
static TypeId GetTypeId (void)
{
static TypeId tid = TypeId ("MyObject")
.SetParent (Object::GetTypeId ())
.AddConstructor<MyObject> ()
.AddTraceSource ("MyInteger",
"An integer value to trace.",
MakeTraceSourceAccessor (&MyObject::m_myInt));
return tid;
}
MyObject () {}
TracedValue<int32_t> m_myInt;
};
void IntTrace (int32_t oldValue, int32_t newValue)
{
std::cout << "Traced " << oldValue << " to " << newValue << std::endl;
}
int main (int argc, char *argv[])
{
Ptr<MyObject> myObject = CreateObject<MyObject> ();
myObject->TraceConnectWithoutContext ("MyInteger", MakeCallback (&IntTrace));
myObject->m_myInt = 1234;
}
Trace source
Trace sink
Connection
Goal: trace changes made to a variable
i.e., notify user whenever
  +, ++, =, etc.

## Slide 8: A simple-low level example: the trace source
class MyObject : public Object
{
public:
static TypeId GetTypeId (void)
{
static TypeId tid = TypeId ("MyObject")
.SetParent (Object::GetTypeId ())
.AddConstructor<MyObject> ()
.AddTraceSource ("MyInteger",
"An integer value to trace.",
MakeTraceSourceAccessor (&MyObject::m_myInt));
return tid;
}
MyObject () {}
TracedValue<int32_t> m_myInt;
};
MyObject is derived from Object, inherits public members
always need GetTypeId method for an object
provides run-time info on type
allows objects to located via path (more on this later)
provides objects with attributes
provides objects with trace sources

## Slide 9: A simple-low level example: the trace source
class MyObject : public Object
{
public:
static TypeId GetTypeId (void)
{
static TypeId tid = TypeId ("MyObject")
.SetParent (Object::GetTypeId ())
.AddConstructor<MyObject> ()
.AddTraceSource ("MyInteger",
"An integer value to trace.",
MakeTraceSourceAccessor (&MyObject::m_myInt));
return tid;
}
MyObject () {}
TracedValue<int32_t> m_myInt;
};
TypeId class records meta-information about MyObject
Provides unique identifier
Record TypeId of base class
Default constructor is accessible
Provides hook to connect to trace source:
Name of source
Help string
Accessor = pointer to connect
Provides infrastructure to
Overload operators
Drive callback process

## Slide 10: A simple low-level example: the trace sink
void IntTrace (int32_t oldValue, int32_t newValue)
{
std::cout << "Traced " << oldValue << " to " << newValue << std::endl;
}
A simple void function
Takes in the old and new values of the traced variable
  Will be supplied by the trace source
Prints them to the screen

## Slide 11: A low-level example: the main function
int main (int argc, char *argv[])
{
Ptr<MyObject> myObject = CreateObject<MyObject> ();
myObject->TraceConnectWithoutContext ("MyInteger", MakeCallback (&IntTrace));
myObject->m_myInt = 1234;
}
NS3 smart pointers provide garbage collection via reference counting
Track number of pointers to an object
Helps avoid memory leaks when you forget to delete an object
Wrapper for C++ “new”
Connecting source to sink
“MyInteger” = name of source
Callback made from our sink function
We’ll talk about “Context” next…
If all goes as planned: should trigger callback

## Slide 12: A low-level example: running fourth.cc
cp examples/tutorial/fourth.cc scratch/myfourth.cc
./waf --run scratch/myfourth
Traced 0 to 1234
Seems almost anticlimactic, but we’ve illustrated the main steps in tracing
Define trace source
Define trace sink
Connect trace source to trace sink
Assignment in: myObject->m_myInt = 1234;
triggers callback

## Slide 13: Using Config to connect to trace sources
TraceConnectWithoutContext is not typical way to connect source to sink
Normally done via the Config subsystem in ns3, by using a config path
  A string that looks like a file path
  Represents chain of objects leading to the desired event (or attribute)
We encountered this in third.cc
”/NodeList/7/$ns3::MobilityModel/CourseChange"
Provides a path to the “CourseChange” attribute for node index 7
Let’s dissect this config path

## Slide 14: Dissecting the Config path in third.cc
“NodeList” = predefined namespace in Config, lists all the nodes in the sim
"NodeList/7" = node 7 (i.e., the eigth node)
"$" = what follows designates an aggregated object
”/NodeList/7/$ns3::MobilityModel/CourseChange"
Let’s take a short detour to discuss aggregated objects in NS3

## Slide 15: Object aggregation in NS3
Makes it possible for objects to access each other, and for users to easily access objects in an aggregation
Avoids need to modify a base class to provide pointers to all possible connected objects
  Class definitions would bloat uncontrollably
  Solution: separate functionality belongs to separate classes
node
mobility
node
mobility
Node->AggregateObject(mobility);
Retrieving an aggregated object:
Ptr<MobilityModel> mob = node->GetObject<MobilityModel> ();

## Slide 16: Dissecting the Config path in third.cc
“NodeList” = predefined namespace in Config, lists all the nodes in the sim
"NodeList/7" = node 7 (i.e., the eigth node)
"$" = what follows designates an aggregated object
"/NodeList/7/$ns3::MobilityModel" = get the mobility model object aggregated to node 7 in the sim
"CourseChange" = attribute of MobilityModel we are interested in
Config will follow the chain of pointers to the attribute you specified
”/NodeList/7/$ns3::MobilityModel/CourseChange"
Ties the trace source to the trace sink callback function
Passes the context (= config path) to the callback function
Config::Connect(”/NodeList/7/$ns3::MobilityModel/CourseChange”,MakeCallback(&CourseChange))

## Slide 17: How to Find and Connect Trace Sources, and Discover Callback Signatures
What trace sources are available (besides CourseChange)?
How do I figure out the config path I need to connect to this source?
What are the return type and arguments of my callback function?
void CourseChange(std::string context,Ptr<const MobilityModel> model)
Void IntTrace (int32_t oldValue, int32_t newValue)
Doxygen and a little detective work will go a long way here

## Slide 18: What trace sources are available?
Doxygen has the answer!
  Trace sources: http://www.nsnam.org/docs/release/3.16/doxygen/group___trace_source_list.html
  Attributes: http://www.nsnam.org/docs/release/3.16/doxygen/group___attribute_list.html
  Global values: http://www.nsnam.org/docs/release/3.16/doxygen/group___global_value_list.html

## Slide 19: What trace sources are available?

## Slide 20: What string do I use to connect?
method 1: look for config path in someone else’s code
  find -name "*.cc" | xargs grep CourseChange | grep Connect
  Config path = "/NodeList/*/$ns3::MobilityModel/CourseChange”
    you can use regular expressions in the path, so "*" ⇒ any node
    "/NodeList/[3-5]∣8∣[0-1]" would match node indices 0,1,3,4,5,8
⋮
./src/mobility/examples/main-random-walk.cc: Config::Connect ("/NodeList/*/$ns3::MobilityModel/CourseChange",
⋮

## Slide 21: What string do I use to connect?
method 2: Doxygen
RandomWalk2dMobilityModel

## Slide 22: What string do I use to connect?
method 2: Doxygen
We’re almost there! We found:
"NodeList/7/$ns3::MobilityModel/CourseChange"
Remember: before, we used:
But what’s this bit?
Scroll further down

## Slide 23: What string do I use to connect?
method 2: Doxygen
This tells you to access the “CourseChange” attribute from the parent class, so:
"NodeList/7/$ns3::MobilityModel/CourseChange"

## Slide 24: What are the return value and arguments for the callback function?
The easy way: copy someone else’s answer
  find -name "*.cc" | xargs grep CourseChange | grep Connect
  Inside “./src/mobility/examples/main-random-walk.cc”:
  And we then find the header of the “CourseChange” function:
./src/mobility/examples/main-random-walk.cc: Config::Connect ("/NodeList/*/$ns3::MobilityModel/CourseChange”,
Config::Connect ("/NodeList/*/$ns3::MobilityModel/CourseChange",
MakeCallback (&CourseChange));
static void CourseChange (std::string foo, Ptr<const MobilityModel> mobility)
But what if you can’t find what you need in someone else’s code?

## Slide 25: What return value and arguments for the callback function?
The somewhat easy way
  The return value is always “void”
  To get the list of formal arguments, look in the ".h" file for the model
    Find the "TracedCallback" declaration
    For ex,in "src/mobility/model/mobility-model.h”
    So for callback using Config::ConnectWithoutContext
    And for callback using Config::Connect
TracedCallback<Ptr<const MobilityModel> > m_courseChangeTrace;
This is the argument we need!
void CourseChange(Ptr<const MobilityModel> model)
void CourseChange(std::string path,Ptr<const MobilityModel> model)
Context (= config path) gets passed here

## Slide 26: What about TracedValue?
Remember we used the callback function
How did we guess the right formal arguments to use?
Find "TracedCallback" declaration in "src/core/model/traced-value.h”
In fourth.cc, inside the MyObject class, we declared
  T = int32_t
  Two arguments in the callback, both of type T (i.e., int32_t)
void IntTrace(int32_t oldValue, int32_t newValue)
template <typename T> class TracedValue
{
public:
...
private:
T m_v;
TracedCallback<T,T> m_cb;
};
Template class ⇒ you get to choose its type
  TracedValue<int32_t> m_myInt;

## Slide 27: A real example
From W. Richard Stevens, “TCP/IP Illustrated, Vol. I: The Protocols”, Addison-Wesley (1994)
Goal: simulate a TCP congestion window and look at the effect of dropped packets
Congestion window

## Slide 28: Congestion windows 101 (from Wikipedia)
Congestion collapse occurs at choke points in the network
  Wherever total incoming traffic to a node > outgoing bandwidth
  e.g., connection points between LAN and WAN
TCP uses network congestion avoidance algorithm
Congestion window is part of TCP strategy to avoid congestion collapse
  Limits total number of unacknowledged packets that may be in transit
  The size of the window is adjusted dynamically by the sender
    Based on how much congestion between sender and receiver
    If all segments are received and the acks reach the sender on time
      Add a constant to the window (typically 1 MSS = Max Segment Size)
    Otherwise
      Scale back by a set factor (typically 1/2)
Explains “sawtooth” shape of congestion window over time

## Slide 29: Are there trace sources available?
From Doxygen’s "The list of all trace sources"
Look for “congestion”:
Click on “ns3::TcpNewReno” to access class info
We have our trace source:
CongestionWindow

## Slide 30: Are there trace sources available?
From Doxygen’s "The list of all trace sources"
Click on link to header file “tcp-newreno.h”
Look for keyword “congestion”

## Slide 31: Are there trace sources available?
From Doxygen’s "The list of all trace sources"
TracedValue<uint32_t> m_cWnd; //< Congestion window
this looks a lot like our fourth.cc example
we'll need a callback function of the form
void CwndTrace(uint32_t oldValue,uint32_t newValue)

## Slide 32: How do we get started writing our script?
The time-honored way: steal from someone else’s code
  find . -name “*.cc” | xargs grep CongestionWindow
  Look, e.g., in “./src/test/ns3tcp/ns3tcp-cwnd-test-suite.cc”
  The connection between trace and source is done by
  We can also copy code from the function
ns3TcpSocket->TraceConnectWithoutContext ("CongestionWindow", MakeCallback (&Ns3TcpCwndTestCase1::CwndChange, this));
void CwndChange (uint32_t oldCwnd, uint32_t newCwnd)
This is the callback function
void Ns3TcpCwndTestCase1::DoRun (void)
This is how fifth.cc was put together

## Slide 33: Avoiding a common mistake in NS3
NS3 scripts execute in three separate stages
  Configuration time
  Simulation time (i.e., Simulator::Run)
  Teardown time
TCP uses sockets to connect nodes
  Sockets are created dynamically during simulation time
    Want to hook the CongestionWindow on the socket of the sender
  Connection to trace sources is established during configuration time
  Can’t put the cart before the horse!
Solution:
  Create socket at configuration time
  Hook trace source then
  Pass this socket object to system during simulation time
Next: fifth.cc walkthrough

## Slide 34: Overview of fifth.cc
Dumbbell topology, point-to-point network, like first.cc
We will create our own application and socket
  So we can access socket at configuration time
  No helper, so we’ll have to do the work manually
  Connect to CongestionWindow trace source in sender socket
Introduce errors into the channel between nodes
  Dropped packets ⇒ interesting behavior in congestion window
0
1
Sender
Receiver

## Slide 35: Creating our own application: the MyApp class
class MyApp : public Application
{
public:
MyApp ();
virtual ~MyApp();
void Setup (Ptr<Socket> socket, Address address, uint32_t packetSize, uint32_t nPackets, DataRate dataRate);
private:
virtual void StartApplication (void);
virtual void StopApplication (void);
void ScheduleTx (void);
void SendPacket (void);
Ptr<Socket> m_socket;
Address m_peer;
uint32_t m_packetSize;
uint32_t m_nPackets;
DataRate m_dataRate;
EventId m_sendEvent;
bool m_running;
uint32_t m_packetsSent;
};
But this is the important bit: we will be able to
Create socket
Hook its CongestionWindow trace source
Pass the socket to the application
All this at configuration time!
Initializes member variables

## Slide 36: Creating our own application: the MyApp class
class MyApp : public Application
{
public:
MyApp ();
virtual ~MyApp();
void Setup (Ptr<Socket> socket, Address address, uint32_t packetSize, uint32_t nPackets, DataRate dataRate);
private:
virtual void StartApplication (void);
virtual void StopApplication (void);
void ScheduleTx (void);
void SendPacket (void);
Ptr<Socket> m_socket;
Address m_peer;
uint32_t m_packetSize;
uint32_t m_nPackets;
DataRate m_dataRate;
EventId m_sendEvent;
bool m_running;
uint32_t m_packetsSent;
};
We also need to override these with our own implementations that will be called by the simulator to start and stop

## Slide 37: Creating our own application: the MyApp class
class MyApp : public Application
{
public:
MyApp ();
virtual ~MyApp();
void Setup (Ptr<Socket> socket, Address address, uint32_t packetSize, uint32_t nPackets, DataRate dataRate);
private:
virtual void StartApplication (void);
virtual void StopApplication (void);
void ScheduleTx (void);
void SendPacket (void);
Ptr<Socket> m_socket;
Address m_peer;
uint32_t m_packetSize;
uint32_t m_nPackets;
DataRate m_dataRate;
EventId m_sendEvent;
bool m_running;
uint32_t m_packetsSent;
};
1
2
3
StartApplication calls SendPacket
SendPacket calls ScheduleTx
ScheduleTx set up next SendPacket call
…
Until StopApplication

## Slide 38: The trace sinks
We want to trace 2 types of events
  Updates to the congestion window:
  Dropped packets
static void CwndChange (uint32_t oldCwnd, uint32_t newCwnd)
{
NS_LOG_UNCOND (Simulator::Now ().GetSeconds () << "\t" << newCwnd);
}
static void RxDrop (Ptr<const Packet> p)
{
NS_LOG_UNCOND ("RxDrop at " << Simulator::Now ().GetSeconds ());
}

## Slide 39: Introducing errors in the channel
Determines which packets are errored corresponding to underlying
Distribution = random variable
Rate ↔ mean duration between errors
Unit = per-bit, per-byte, or per-packet
Ptr<RateErrorModel> em = CreateObjectWithAttributes<RateErrorModel> (
"RanVar", RandomVariableValue (UniformVariable (0., 1.)),
"ErrorRate", DoubleValue (0.00001));
devices.Get (1)->SetAttribute ("ReceiveErrorModel", PointerValue (em));
Will cause randomly dropped packets in the receiver device

## Slide 40: Setting the application on the receiver node
uint16_t sinkPort = 8080;
Address sinkAddress (InetSocketAddress (interfaces.GetAddress (1), sinkPort));
PacketSinkHelper packetSinkHelper ("ns3::TcpSocketFactory", InetSocketAddress (Ipv4Address::GetAny (), sinkPort));
ApplicationContainer sinkApps = packetSinkHelper.Install (nodes.Get (1));
sinkApps.Start (Seconds (0.));
sinkApps.Stop (Seconds (20.));
PacketSink receives and consumes traffic generated to an IP address and port
PacketSinkHelper creates sockets using an “object factory”
  Object factories are used to mass produce similarly configured objects
  Factory method doesn’t require you to know the type of the objects created

## Slide 41: Connecting the sender’s socket, and connecting the trace source
Ptr<Socket> ns3TcpSocket = Socket::CreateSocket (nodes.Get (0), TcpSocketFactory::GetTypeId ());
ns3TcpSocket->TraceConnectWithoutContext ("CongestionWindow", MakeCallback (&CwndChange));
Another way of creating a socket using a socket factory
This should look familiar by now
Because we created our own app and socket at configuration time we can hook into its CongestionWindow trace source

## Slide 42: Setting up the application on the sender node
Ptr<MyApp> app = CreateObject<MyApp> ();
app->Setup (ns3TcpSocket, sinkAddress, 1040, 1000, DataRate ("1Mbps"));
nodes.Get (0)->AddApplication (app);
app->SetStartTime (Seconds (1.));
app->SetStopTime (Seconds (20.));
Socket object
Address to connect to
Data per send event
Number of send events
Send data rate

## Slide 43: Running fifth.cc: text output
./waf –run scratch/myfifth > cwnd.dat 2>&1
Waf: Entering directory `/mypath/ns-3-dev/build'
Waf: Leaving directory `/mypath/ns-3-dev/build'
'build' finished successfully (1m58.520s)
1 536
1.00919 1072
1.01511 1608
1.02163 2144
1.02995 2680
1.03827 3216
1.04659 3752
1.05491 4288
1.06323 4824
1.07155 5360
1.07987 5896
1.08819 6432
1.09651 6968
1.10483 7504
1.11315 8040
1.12147 8576
1.12979 9112
RxDrop at 1.13692
1.13811 9648
1.15475 2900
1.15563 3436
⋮
Eliminate these lines by hand

## Slide 44: Running fifth.cc: plotting the results
Original by W. Richard Stevens
Our result, using gnuplot

## Slide 45: That’s nice, but…
Remember after
We had to edit the file by hand to remove “junk” lines…
But we said tracing gives you control over output format
Is there a cleaner way to produce the output we need?
Yes! Use trace helpers
./waf –run scratch/myfifth > cwnd.dat 2>&1
Let’s tweak fifth.cc to produce cleaner output ⇒ sixth.cc

## Slide 46: A sixth.cc walkthrough: CwndChange callback
static void CwndChange (Ptr<OutputStreamWrapper> stream, uint32_t oldCwnd, uint32_t newCwnd)
{
NS_LOG_UNCOND (Simulator::Now ().GetSeconds () << "\t" << newCwnd);
*stream->GetStream () << Simulator::Now ().GetSeconds () << "\t" << oldCwnd << "\t" << newCwnd << std::endl;
}
Added to fifth.cc
Modify the callback function:
Add lines in the main to create stream:
Causes the stream argument to be added to the function callback
Formatted output to the stream
AsciiTraceHelper asciiTraceHelper;
Ptr<OutputStreamWrapper> stream = asciiTraceHelper.CreateFileStream ("sixth.cwnd");
ns3TcpSocket->TraceConnectWithoutContext ("CongestionWindow", MakeBoundCallback (&CwndChange, stream));
Filename attached to stream

## Slide 47: A sixth.cc walkthrough: RxDrop callback
Added to fifth.cc
Modify the callback function:
Add lines in the main to create stream:
Causes the file argument to be added to the function callback
Formatted output to the pcap file
Filename attached to file
static void RxDrop (Ptr<PcapFileWrapper> file, Ptr<const Packet> p)
{
NS_LOG_UNCOND ("RxDrop at " << Simulator::Now ().GetSeconds ());
file->Write (Simulator::Now (), p);
}
PcapHelper pcapHelper;
Ptr<PcapFileWrapper> file = pcapHelper.CreateFile ("sixth.pcap", std::ios::out, PcapHelper::DLT_PPP);
devices.Get (1)->TraceConnectWithoutContext ("PhyRxDrop", MakeBoundCallback (&RxDrop, file));

## Slide 48: Running sixth.cc
./waf –run scratch/mysixth
Waf: Entering directory `…
Waf: Leaving directory `…
'build' finished successfully (6.002s)
1 536
1.00919 1072
1.01511 1608
1.02163 2144
1.02995 2680
1.03827 3216
1.04659 3752
1.05491 4288
1.06323 4824
1.07155 5360
1.07987 5896
1.08819 6432
1.09651 6968
1.10483 7504
1.11315 8040
1.12147 8576
1.12979 9112
RxDrop at 1.13692
1.13811 9648
1.15475 2900
1.15563 3436
⋮
Console
sixth.cwnd
1 0 536
1.00919 536 1072
1.01511 1072 1608
1.02163 1608 2144
1.02995 2144 2680
1.03827 2680 3216
1.04659 3216 3752
1.05491 3752 4288
1.06323 4288 4824
1.07155 4824 5360
1.07987 5360 5896
1.08819 5896 6432
1.09651 6432 6968
1.10483 6968 7504
1.11315 7504 8040
1.12147 8040 8576
1.12979 8576 9112
1.13811 9112 9648
⋮
reading from file sixth.pcap, link-type PPP (PPP)
1.136918 IP 10.1.1.1.49153 > 10.1.1.2.8080: Flags [.], seq 17177:17681, ack 1, win 65535, length 504
1.403158 IP 10.1.1.1.49153 > 10.1.1.2.8080: Flags [.], seq 33280:33784, ack 1, win 65535, length 504
1.440505 IP 10.1.1.1.49153 > 10.1.1.2.8080: Flags [.], seq 37440:37944, ack 1, win 65535, length 504
2.525484 IP 10.1.1.1.49153 > 10.1.1.2.8080: Flags [.], seq 173144:173680, ack 1, win 65535, length 536
2.534678 IP 10.1.1.1.49153 > 10.1.1.2.8080: Flags [.], seq 174720:175224, ack 1, win 65535, length 504
2.977574 IP 10.1.1.1.49153 > 10.1.1.2.8080: Flags [.], seq 180552:181088, ack 1, win 65535, length 536
5.796117 IP 10.1.1.1.49153 > 10.1.1.2.8080: Flags [.], seq 582400:582904, ack 1, win 65535, length 504
6.445077 IP 10.1.1.1.49153 > 10.1.1.2.8080: Flags [.], seq 663520:664024, ack 1, win 65535, length 504
7.359404 IP 10.1.1.1.49153 > 10.1.1.2.8080: Flags [.], seq 777384:777920, ack 1, win 65535, length 536
7.389304 IP 10.1.1.1.49153 > 10.1.1.2.8080: Flags [.], seq 781040:781544, ack 1, win 65535, length 504
8.141483 IP 10.1.1.1.49153 > 10.1.1.2.8080: Flags [.], seq 875144:875680, ack 1, win 65535, length 536
sixth.pcap

## Slide 49: Just for fun: what happens to uncorrupted packets?
PhyRxEnd: Trace source indicating a packet has been completely received by the device

## Slide 50: Using trace helpers
We’ve encountered trace helpers before
What other trace helpers are available?
How do we use them?
What do they have in common?
pointToPoint.EnablePcapAll ("second");
pointToPoint.EnablePcap ("second", p2pNodes.Get (0)->GetId (), 0);
csma.EnablePcap ("third", csmaDevices.Get (0), true);
pointToPoint.EnableAsciiAll (ascii.CreateFileStream ("myfirst.tr"));

## Slide 51: Two categories of trace helpers
Device helpers
  Trace is enabled for node/device pair(s)
  Both pcap and ascii traces provided
  Conventional filenames: <prefix>-<node id>-<device id>
Protocol helpers
  Trace is enabled for protocol/interface pair(s)
  Both pcap and ascii traces provided
  Conventional filenames: <prefix>-n<node id>-i<interface id>
    “n” and “i” to avoid filename collisions with node/device traces

## Slide 52: NS3 uses “mixin” classes to ensure tracing works the same way across all devices or interfaces
Mixin classes in NS3 (see Doxygen for more info):
These mixin classes each provide a single virtual method to enable trace
  All device or protocols must implement this method
  All other methods of the mixin class call this one method
  Provides consistent functionality across different devices & interfaces
 | PCAP | ASCII
Device Helper | PcapHelperForDevice | AsciiTraceHelperForDevice
Protocol Helper | PcapHelperForIpv4 | AsciiTraceHelperForIpv4

## Slide 53: The PcapHelperForDevice mixin class
Every device must implement
All other methods of PcapHelperForDevice call this one
⇒ Consistency across devices
virtual void EnablePcapInternal (std::string prefix,
Ptr<NetDevice> nd,
bool promiscuous,
bool explicitFilename) = 0;
Pcap filename prefix
Device to trace
Type of trace
Override prefix

## Slide 54: Pcap Tracing Device Helper: EnablePcap methods
EnablePcap for various node/device pair(s)
  Provide Ptr<NetDevice>
  Provide device name using the NS3 object name service
  Provide a NetDeviceContainer
  Provide a NodeContainer
  Provide integer node and device ids
Enable pcap tracing for all devices in the simulation
Names::Add ("server" ...);
Names::Add ("server/eth0" ...);
...
helper.EnablePcap ("prefix", "server/ath0");
helper.EnablePcapAll ("prefix");

## Slide 55: Pcap Tracing Device Helper: filename selection
  By convention: <prefix>-<node id>-<device id>.pcap
  Can use the NS3 object name service to replace ids with meaningful names e.g.,
  You can override the naming convention, e.g.
Names::Add(“server”,serverNode);
Names::Add(“server/eth0”,serverDevice);
prefix-21-1.pcap
prefix-server-eth0.pcap
Set this to true
prefix becomes filename
void EnablePcap(std::string prefix, Ptr<NetDevice> nd, bool promiscuous, bool explicitFilename);

## Slide 56: Ascii Tracing Device Helpers
  The mixin class is AsciiTraceHelperForDevice
  All device implement virtual EnableAsciiInternal method
  All other methods of AsciiTraceHelperForDevice will call this one
  Can provide EnableAscii with Ptr<NetDevice>, string from name service, NetDeviceContainer, NodeContainer, integer node/device ids
  Or helper.EnableAsciiAll(“prefix”);
  Can also dump ascii traces to a single common file, e.g.,
  So there are twice as many trace methods as for pcap
Ptr<NetDevice> nd1;
Ptr<NetDevice> nd2;
...
Ptr<OutputStreamWrapper> stream = asciiTraceHelper.CreateFileStream ("trace-file-name.tr");
...
helper.EnableAscii (stream, nd1);
helper.EnableAscii (stream, nd2);

## Slide 57: Ascii Tracing Device Helpers: filename selection
By convention: <prefix>-<node id>-<device id>.tr
Using NS3 object name service, can assign names to the id, then e.g.
  "prefix-21-1.tr” → "prefix-server-eth0.tr”
Many EnableAscii methods offer a explicitFilename option
  set to true ⇒ override naming convention, use your own file name

## Slide 58: Pcap Tracing Protocol Helpers
  The mixin class is PcapHelperForIpv4
  All device implement virtual EnablePcapIpv4Internal method
  All other methods of PcapHelperForIpv4 will call this one
  Can provide EnablePcapIpv4 with Ptr<Ipv4>, string from name service, Ipv4InterfaceContainer, NodeContainer, integer node/device ids
  Or helper.EnablePcapIpv4All(“prefix”);
  Filename selection
    Convention is <prefix>-n<node id>-i<interface id>.pcap
    Can also use the NS3 object name service clarity
    explicitFilename parameter lets you impose your own filenames

## Slide 59: Ascii Tracing Protocol Helpers
  The mixin class is AsciiTraceHelperForIpv4
  All device implement virtual EnableAsciiIpv4Internal method
  All other methods of AsciiTraceHelperForIpv4 will call this one
  Can provide EnableAsciiIpv4 with Ptr<Ipv4>, string from name service, Ipv4InterfaceContainer, NodeContainer, integer node/device ids
  Or helper.EnableAsciiIpv4All(“prefix”);
  Can also dump ascii traces to a single common file
    So there are twice as many trace methods as for pcap
  Filename selection
    Convention is <prefix>-n<node id>-i<interface id>.pcap
    Can also use the NS3 object name service clarity
    explicitFilename parameter lets you impose your own filenames

## Slide 60: Conclusion
NS3 is very powerful/comprehensive
Lots of tools for you to use
  Helpers
  Containers
  Logging
  Tracing
  Models
Doxygen is your friend!
Practice! Practice! Practice!