## Slide 1
ns-3 Training

## Slide 2: Outline
Emulation modes
  Tap Bridge
  FdNetDevice
Direct Code Execution (DCE)
  Applications
  Linux Kernel
  DCE Cradle

## Slide 3: Emulation support
Support moving between simulation and testbeds or live systems
A real-time scheduler, and support for two modes of emulation
Linux is only operating system supported
Must run simulator in real time
  GlobalValue::Bind (“SimulatorImplementationType”, StringValue (“ns3::RealTimeSimulatorImpl”));
Must enable checksum calculations across models
  GlobalValue::Bind (“ChecksumEnabled”, BooleanValue (true));
Must run as root

## Slide 4: ns-3 emulation modes
virtual
machine
ns-3
virtual
machine
1) ns-3 interconnects real or virtual machines
real
machine
ns-3
Testbed
real
machine
ns-3
2) testbeds interconnect ns-3 stacks
real machine
Various hybrids of the above are possible

## Slide 5: Example use case: testbeds
Support for use of Rutgers WINLAB ORBIT radio grid

## Slide 6: Example use case: PlanetLab
The PlanetLabFdNetDeviceHelper creates TAP devices on PlanetLab nodes using specific PlanetLab mechanisms (i.e. the vsys system), and associates the TAP device to a FdNetDevice in ns-3.

## Slide 7: Example use case: mininet
Mininet is popular in the Software-Defined Networking (SDN) community
Mininet uses "TapBridge" integration
  https://github.com/mininet/mininet/wiki/Link-modeling-using-ns-3

## Slide 8: Emulation Devices

## Slide 9: Device models
File Descriptor Net Device (FdNetDevice)
  read and write traffic using a file descriptor provided by the user
  this file descriptor can be associated to a TAP device, to a raw socket, to a user space process generating/consuming traffic, etc.
Tap Bridge
  Integrate Tun/Tap devices with ns-3 devices

## Slide 10: “TapBridge": netns and ns-3 integration
Container
ns-3
Linux
tapX
/dev/tunX
TapBridge
WiFi
ghost node
Wifi
ghost node
tapY
Tap device pushed into namespaces; no bridging needed
/dev/tunY
Container
TapBridge
WiFi

## Slide 11: TapBridge modes
ConfigureLocal (default mode)
  ns-3 configures the tap device
  useful for host to ns-3 interaction
UseLocal
  user has responsibility for device creation
  ns-3 informed of device using “DeviceName” attribute
UseBridge
  TapDevice connected to existing Linux bridge

## Slide 12: ConfigureLocal
ns-3 ensures that Mac addresses
are consistent

## Slide 13: UseLocal
Mac X spoofed to Mac Y

## Slide 14: UseBridge
ns-3 devices must support SendFrom()
(i.e. bridging)

## Slide 15: FdNetDevice
Unified handling of reading/writing from file descriptor
Three supported helper configurations:
  EmuFdNetDeviceHelper (to associate the ns-3 device with a physical device in the host machine)
  TapFdNetDeviceHelper (to associate the ns-3 device with the file descriptor from a tap device in the host machine) (not the same as TapBridge)
  PlanetLabFdNetDeviceHelper (to automate the creation of tap devices in PlanetLab nodes, enabling ns-3 simulations that can send and receive traffic though the Internet using PlanetLab resource.

## Slide 16: EmuFdNetDeviceHelper
Device performs MAC spoofing to separate emulation from host traffic

## Slide 17: PlanetLabFdNetDeviceHelper
Special case of TapFdNetDeviceHelper where Tap devices configured according to PlanetLab conventions

## Slide 18: ns-3 over host sockets
Two publications about how to run ns-3 applications over real hosts and sockets
  "Simulator-agnostic ns-3 Applications", Abraham and Riley, WNS3 2012
  Gustavo Carneiro, Helder Fontes, Manuel Ricardo, "Fast prototyping of network protocols through ns-3 simulation model reuse", Simulation Modelling Practice and Theory (SIMPAT), vol. 19, pp. 2063–2075, 2011.

## Slide 19: Generic Emulation Issues
Ease of use
  Configuration management and coherence
  Information coordination (two sets of state)
    e.g. IP/MAC address coordination
  Output data exists in two domains
  Debugging can be more challenging
Error-free operation (avoidance of misuse)
  Synchronization, information sharing, exception handling
    Checkpoints for execution bring-up
    Inoperative commands within an execution domain
    Deal with run-time errors
  Soft performance degradation (CPU) and time discontinuities