## Slide 1
ns-3 Training

## Slide 2: Outline
Wi-Fi in detail
  Support of standard features
  Architecture
  Configuration via helpers
Advanced use case: LAA-Wifi-Coexistence
  SpectrumWifiPhy
  Adding a LBT Access Manager
  Scenario support
  Output data processing

## Slide 3: Wi-Fi Overview
WiFi module features
  DCF implementation (Basic + RTS/CTS)
  802.11 a/b/g/n/ac (2.4 & 5 GHz) PHY
  MSDU/MPDU aggregation
  QoS support (EDCA)
  Infrastructure and ad-hoc modes
  Many rate adaptation algorithms
  AWGN-based error models
Unsupported features
  MIMO
  11ac advanced features (Tx beamforming, Mu-MIMO)
Related modules
  Mesh (802.11s) and WAVE (802.11p/vehicular)

## Slide 4: Current Wi-Fi PHY abstraction

## Slide 5
Spectrum Module
Three key pieces
  SpectrumValue, SpectrumChannel, SpectrumPhy
SpectrumValue is the signal abstraction being passed through to the channel (and to the users)
  A vector of sub-bands representing center frequency, bandwidth, and sub-band power specral density
SpectrumChannel delays/attenuates/modifies the transmitted signal as specified before providing copies to all receivers
  Automatically converts signals with different resolutions
Inheriting from SpectrumPhy allows different types of devices to interact through the wireless channel
SpectrumChannel
Dev 1
(SpectrumPhy)
Dev 2
(SpectrumPhy)
Dev N
(SpectrumPhy)
SpectrumValue
SpectrumValue
SpectrumValue

## Slide 6: Nodes, Mobility, and Position
ALL nodes have to be created before simulation starts
Position Allocators setup initial position of nodes
  List, Grid, Random position…
Mobility models specify how nodes will move
  Constant position, constant velocity/acceleration, waypoint…
  Trace-file based from mobility tools such as SUMO, BonnMotion (using NS2 format)
  Routes Mobility using Google API (*)
(*) Presented in WNS3 - 2015

## Slide 7: Position Allocation Examples
  List MobilityHelper mobility; // place two nodes at specific positions (100,0) and (0,100) Ptr<ListPositionAllocator> positionAlloc = CreateObject<ListPositionAllocator> (); positionAlloc->Add (Vector (100, 0, 0)); positionAlloc->Add (Vector (0, 100, 0)); mobility.SetPositionAllocator(positionAlloc);
Grid Position
  MobilityHelper mobility;
  // setup the grid itself: nodes are laid out started from (-100,-100) with 20 per row, the x
  // interval between each object is 5 meters and the y interval between each object is 20 meters
  mobility.SetPositionAllocator ("ns3::GridPositionAllocator",
  "MinX", DoubleValue (-100.0),
  "MinY", DoubleValue (-100.0),
  "DeltaX", DoubleValue (5.0),
  "DeltaY", DoubleValue (20.0),
  "GridWidth", UintegerValue (20),
  "LayoutType", StringValue ("RowFirst"));
Random Rectangle Position
  // place nodes uniformly on a straight line from (0, 1000)
  MobilityHelper mobility;
  Ptr<RandomRectanglePositionAllocator> positionAloc = CreateObject<RandomRectanglePositionAllocator>();
  positionAloc->SetAttribute("X", StringValue("ns3::UniformRandomVariable[Min=0.0|Max=100.0]"));
  positionAloc->SetAttribute("Y", StringValue("ns3::ConstantRandomVariable[Constant=50.0]"));
  mobility.SetPositionAllocator(positionAloc);

## Slide 8: Mobility Model Example
Constant Position
  MobilityHelper mobility;
  mobility.SetMobilityModel ("ns3::ConstantPositionMobilityModel");
  mobility.Install (nodes);
Constant Speed
  MobilityHelper mobility;
  mobility.SetMobilityModel ("ns3::ConstantVelocityMobilityModel");
  mobility.Install (nodes);
  Ptr<UniformRandomVariable> rvar = CreateObject<UniformRandomVariable>();
  for (NodeContainer::Iterator i = nodes.Begin (); i != nodes.End (); ++i){
  Ptr<Node> node = (*i);
  double speed = rvar->GetValue(15, 25);
  node->GetObject<ConstantVelocityMobilityModel>()->SetVelocity(Vector(speed,0,0));
  }
Trace-file based
  std::string traceFile = “mobility_trace.txt”;
  // Create Ns2MobilityHelper with the specified trace log file as parameter
  Ns2MobilityHelper ns2 = Ns2MobilityHelper (traceFile);
  ns2.Install (); // configure movements for each node, while reading trace file
Notes: Explain key differences of these models and under what situations would I use each one.

## Slide 9: Interesting ns-3 extensions
ns-3-highway-mobility (https://code.google.com/p/ns-3-highway-mobility/)
  Implement IDM and MOBIL change lane, highway class, traffic-lights.
  Based on ns-3.8
  No longer maintained
Virtual Traffic Lights (PROMELA) (https://dsn.tm.kit.edu/misc_3434.php)
  Manhattan IDM mobility model
  NLOS propagation loss models
  (Virtual) Traffic Light applications

## Slide 10: Propagation Models
Propagation Loss
  ITUR1411, LogDistance, ThreeLogDistance, Range, TwoRayGround, Friis
  Nakagami, Jakes
  Obstacle model (*)
Propagation Delay
  Constant Speed
  Random
Be careful when using YansWifiChannelHelper::Default() the LogDistance propagation model is added. Calling AddPropagationLoss() again will add a second propagation loss model.
(*) Presented in WNS3 2015

## Slide 11: Communication Range
Depends on many factors
  Propagation loss model and PHY configuration
  Frame size (big vs small)
  Transmission mode (6Mbps vs 54 Mbps)

## Slide 12: Wi-Fi Architecture

## Slide 13: MAC High
Presently, three MAC high models
  AdhocWifiMac: simplest one
  ApWifiMac: beacon, associations by STAs
  StaWifiMac: association based on beacons
All inherit from RegularWifiMac, which handles QoS and non-QoS support

## Slide 14: Rate controls
The following rate control algorithms can be used by the MAC low layer:
Algorithms found in real devices:
  ArfWifiManager (default for WifiHelper), OnoeWifiManager, ConstantRateWifiManager, MinstrelWifiManager, MinstrelHtWifiManager
Algorithms in literature:
  IdealWifiManager, AarfWifiManager, AmrrWifiManager, CaraWifiManager, RraaWifiManager, AarfcdWifiManager, ParfWifiManager, AparfWifiManager
Example use of constant rate
std::string phyMode ("OfdmRate54Mbps");
wifi.SetRemoteStationManager ("ns3::ConstantRateWifiManager",
"DataMode",StringValue (phyMode),
"ControlMode",StringValue (phyMode));

## Slide 15: MAC Middle/Low
Three components:
MacLow
  RTS/CTS/DATA/ACK transactions
  Aggregation, Block acks
DcfManager
  implements the DCF
DcaTxop and EdcaTxopN:
  One for NQoS, the other for QoS
  Packet queue
  Fragmentation/Retransmissions

## Slide 16: Physical layer
No AGC model
Sync on first RX with energy > detection threshold
Collision: the error model will likely cause a drop of the packet
No capture effect: won’t re-sync on a stronger packet

## Slide 17: Error models
Based on analytical models with error bounds
Three implementations with different bounds: YansErrorRateModel, NistErrorRateModel, DssErrorRateModel
NistErrorRateModel (OFDM)
DsssErrorRateModel

## Slide 18: Interference helper
SINR evaluated on chunk-by-chunk basis

## Slide 19: Configuring 802.11n/ac
Example programs include
  examples/wireless/ht-wifi-network.cc
  examples/wireless/vht-wifi-network.cc
  examples/wireless/wifi-aggregation.cc
Setting the WifiPhyStandard will set most defaults reasonably
  WifiHelper wifi;
  wifi.SetStandard (WIFI_PHY_STANDARD_80211ac);
  WifiMacHelper mac;
802.11ac uses 80 MHz channel by default; 802.11n uses 20 MHz

## Slide 20: 802.11n/ac rate controls
Possible options are IdealWifiManager, MinstrelHtWifiManager, and ConstantRateWifiManager
examples:
  src/wifi/examples/ideal-wifi-manager-example.cc
  src/wifi/examples/minstrel-ht-wifi-manager-example.cc

## Slide 21: Example output for MinstrelHt
$ ./waf --run "minstrel-ht-wifi-manager-example --standard=802.11n-5GHz"
$ gnuplot minstrel-ht-802.11n-5GHz-20MHz-LGI-1SS.plt

## Slide 22: Typical configuration
std::string phyMode ("DsssRate1Mbps");
NodeContainer ap;
ap.Create (1);
NodeContainer sta;
sta.Create (2);
WifiHelper wifi;
wifi.SetStandard (WIFI_PHY_STANDARD_80211b);
YansWifiPhyHelper wifiPhy = YansWifiPhyHelper::Default ();
// ns-3 supports RadioTap and Prism tracing extensions for 802.11
wifiPhy.SetPcapDataLinkType (YansWifiPhyHelper::DLT_IEEE802_11_RADIO);
YansWifiChannelHelper wifiChannel;
// reference loss must be changed since 802.11b is operating at 2.4GHz
wifiChannel.SetPropagationDelay ("ns3::ConstantSpeedPropagationDelayModel");
wifiChannel.AddPropagationLoss ("ns3::LogDistancePropagationLossModel",
"Exponent", DoubleValue (3.0),
"ReferenceLoss", DoubleValue (40.0459));
wifiPhy.SetChannel (wifiChannel.Create ());

## Slide 23: Typical configuration (cont.)
// Add a non-QoS upper mac, and disable rate control
WifiMacHelper wifiMac;
wifi.SetRemoteStationManager ("ns3::ConstantRateWifiManager",
"DataMode",StringValue (phyMode),
"ControlMode",StringValue (phyMode));
// Setup the rest of the upper mac
Ssid ssid = Ssid ("wifi-default");
// setup ap.
wifiMac.SetType ("ns3::ApWifiMac",
"Ssid", SsidValue (ssid));
NetDeviceContainer apDevice = wifi.Install (wifiPhy, wifiMac, ap);
NetDeviceContainer devices = apDevice;
// setup sta.
wifiMac.SetType ("ns3::StaWifiMac",
"Ssid", SsidValue (ssid),
"ActiveProbing", BooleanValue (false));
NetDeviceContainer staDevice = wifi.Install (wifiPhy, wifiMac, sta);
devices.Add (staDevice);

## Slide 24: Typical configuration (cont.)
// Configure mobility
MobilityHelper mobility;
Ptr<ListPositionAllocator> positionAlloc = CreateObject<ListPositionAllocator> ();
positionAlloc->Add (Vector (0.0, 0.0, 0.0));
positionAlloc->Add (Vector (5.0, 0.0, 0.0));
positionAlloc->Add (Vector (0.0, 5.0, 0.0));
mobility.SetPositionAllocator (positionAlloc);
mobility.SetMobilityModel ("ns3::ConstantPositionMobilityModel");
mobility.Install (ap);
mobility.Install (sta);
// other set up (e.g. InternetStack, Application)

## Slide 25: Athstats helper
Hooks Wi-Fi traces to provide debugging similar to Madwifi drivers
Example athstats output from example ./waf --run wifi-ap
m_txCount m_rxCount unused short long exceeded rxError
0 0 0 0 0 0 0 0 0 0 0M
0 60 0 0 0 0 0 0 0 0 0M
0 123 0 0 0 0 0 0 0 0 0M
0 122 0 0 0 0 0 0 0 0 0M
0 122 0 0 0 0 0 0 0 0 0M
0 122 0 0 0 0 0 0 0 0 0M
0 122 0 0 0 0 2 0 0 0 0M
0 122 0 0 0 0 23 0 0 0 0M
0 122 0 0 0 0 14 0 0 0 0M
0 122 0 0 0 0 14 0 0 0 0M
0 122 0 0 0 0 26 0 0 0 0M
0 122 0 0 0 0 12 0 0 0 0M

## Slide 26: LTE/Wi-Fi Coexistence

## Slide 27: Use case: LAA Wi-Fi Coexistence
ns-3 has been extended to support scenarios for LTE LAA/Wi-Fi Coexistence
Methodology defined in 3GPP Technical Report TR36.889
Enhancements needed:
  Wireless models (LBT access manager, SpectrumWifiPhy, propagation/fading models)
  Scenario support (traffic models)
  Output data processing

## Slide 28: Indoor 3GPP scenario

## Slide 29: Indoor scenario details

## Slide 30: Outdoor 3GPP scenario
Outdoor layout: hexagonal macrocell layout. 7 macro sites and 3 cells per site. 1 Cluster per cell. 4 small cells per operator per cluster, uniformly dropped. ITU UMi channel model.
Figure source: 3GPP TR 36.889 V13.0.0 (2015-05)

## Slide 31: References
ns-3 Wiki page:
  https://www.nsnam.org/wiki/LAA-WiFi-Coexistence
    module documentation
    references to various publications
    documentation on reproducing results
Code:
  http://code.nsnam.org/laa/ns-3-lbt

## Slide 32: Sample results

## Slide 33: Wi-Fi enhancements

## Slide 34: Model enhancements: Wi-Fi
Spectrum Wi-Fi Phy implementation
Wi-Fi preamble detection based on AWGN and TGn Channel Model D
Wi-Fi RSS-based AP selection and roaming
Wi-Fi MIMO approximations to support 2x2 DL, 1x2 DL on AWGN and TGn Model D

## Slide 35: Model enhancements: LTE
LTE interference model relies on the simplifying assumption that all interfering signals are LTE and are synchronized at the subframe level.
LTE inteference model has been enhanced to handle inteference by signals of any type.
This relies on the ns-3 Spectrum framework.
The reception of LTE signals is evaluated by chunks, where each chunk is identified by a constant power spectral density.

## Slide 36: Scenario
An initial test scenario, useful for testing basic model operation in a small scale setting, grew into TR36.889-like indoor and outdoor scenarios
D1 and d2 can vary and operator A and B can be both LTE or Wi-Fi

## Slide 37: Output experiment scripts
Shell scripts and gnuplot helpers to manage configuration and data output
(demonstrate)

## Slide 38: Status
Portions are being migrated into ns-3-dev
  SpectrumWifiPhy in ns-3.26
  LTE components, propagation model likely in ns-3.27
  Scenario helper may be rewritten
Trying to decompose into pieces easy to merge
For more information:
  https://www.nsnam.org/wiki/LAA-WiFi-Coexistence