## Slide 1: Proximity Services (ProSe) Support for 5G NR Simulations
WNS3 2023 – June 2023
Aziza Ben Mosbah1,2 and Samantha Gamboa1,2
1 Associate, Wireless Networks Division (WND) - National Institute of Standards and Technology (NIST) - Gaithersburg, Maryland, USA
2 Prometheus Computing LLC - Bethesda, Maryland, USA

## Slide 2: Disclaimer
Certain software is identified in this presentation in order to visualize simulation outputs adequately. Such identification is not intended to imply recommendation or endorsement of any product or service by NIST, nor is it intended to imply that the materials or equipment identified are necessarily the best available for the purpose.

## Slide 3: Outline
Motivation
Current functionalities
Model overview
Code availability and setup
NR ProSe direct discovery
  Overview
  Example -> nr-prose-discovery.cc
  Example -> nr-prose-discovery-l3-relay.cc
NR ProSe unicast communication
  Overview
  Example -> nr-prose-unicast-multi-link.cc
NR ProSe L3 UE-to-Network relay
  Overview
  Example -> nr-prose-l3-relay.cc
NR ProSe L3 U2N Relay selection (Integration direct discovery with L3 U2N relay)
  Example -> nr-prose-discovery-l3-relay-selection.cc

## Slide 4: Motivation
NR Proximity Services (ProSe)
3GPP Rel-17 +
Direct Communication
Broadcast, Groupcast, Unicast
UE-based Relays
UE-to-Network, UE-to-UE
Direct Discovery
Peers, Members, Relays
NR Sidelink
Sensing
Channel awareness
Inter-UE coordination
Feedback
Feedback-based retransmissions
Channel State Information
Scheduling
Semi-persistent
Per-packet
Multicast
Connectionless
Distance-based
QoS
Similar to Uu interface
Enhanced for SL
Spectrum flexibility
Numerologies
Extended modulations
3GPP Rel-16 +
NR Vehicle to Everything (V2X) Services
3GPP Rel-16 +
V2X Communication
Broadcast, Groupcast, Unicast

## Slide 5: Current functionalities
NR Proximity Services (ProSe)
Rel-17 +
Direct Communication
Broadcast, Groupcast, Unicast
UE-based Relays
UE-to-Network, UE-to-UE
Direct Discovery
Peers, Members, Relays
NR ProSe direct discovery
- Direct peer discovery
- UE-to-Network relay discovery
- Model A and Model B
NR ProSe unicast communication
- Direct link establishment
- Traffic exchange between peer UEs
- Multiple direct links with different peers
NR ProSe L3 UE-to-Network relay
- Remote UE to Relay UE connection
- Layer 3 traffic relaying
- Remote UE network transparency
Integration

## Slide 6: Model overview - ProSe over NR SL
APP
PDU layer
SDAP
PDCP
RLC
MAC
PHY
APP
PDU layer
SDAP
PDCP
RLC
MAC
PHY
UE 2
UE 1
PC5
PC5
SL
ProSe
NAS
RRC
ProSe
NAS
RRC
Data
Data
Control
Control
Other protocols
ProSe layer
NR layers
Legend
APP: Application
MAC: Media Access Control
NAS: Non-Access Stratum
PDU: Protocol Data Unit
PDCP: Packet Data Convergence Protocol
PDU: Protocol Data Unit
PHY: Physical Layer
ProSe: Proximity Services
RLC: Radio Link Control
RRC: Radio Resource Control
SL: Sidelink
SDAP: Service Data Adaptation Protocol
UE: User equipment
SDAP
PDCP
RLC
MAC
PHY
SDAP
PDCP
RLC
MAC
PHY
PC5
NR ProSe Protocol Stacks
APP
PDU layer
SDAP
PDCP
RLC
MAC
PHY
APP
PDU layer
SDAP
PDCP
RLC
MAC
PHY
UE 2
UE 1
PC5
PC5
SL
ProSe
NAS
RRC
ProSe
NAS
RRC
Data
Data
Control
Control
SDAP
PDCP
RLC
MAC
PHY
SDAP
PDCP
RLC
MAC
PHY
PC5
NR ProSe Protocol Stacks
(current implementation)
LTE layers
Not implemented
The ProSe model is based on
- CTTC’s NR V2X release v0.1
and
- ns3 ns-3.36
We implemented the ProSe layer and modified other layers to support the ProSe functionalities
NR module
LTE module

## Slide 7: Model overview - UE Control Plane Architecture
NrSlProseHelper
*
*
*
*
*
*
*
*
New class
New SAP
New bearer
Legend
* Modified
NR ProSe simulation typical flow:
During scenario configuration:
- Configure ProSe functionalities using ProSe helper
- Internally the helper installs ProSe layer and configures functionality
During simulation:
- ProSe layer controls functionalities
- Context creation and management
- SL bearer creation/configuration
- Procedures execution
Notes: Transition green first, then purple

## Slide 8: Code availability and setup
How to get started:
1. Get the code and move into psc-ns3 directory:
git clone "https://github.com/usnistgov/psc-ns3.git" -b wns3-2023-nr-prose-preview
cd psc-ns3
2. Setup ns3:
./ns3 configure --enable-examples
./ns3
3. Run examples:
Running a ProSe example:
./ns3 run ‘exampleName’
e.g.,
Running a a ProSe example with command line parameters:
./ns3 run ‘exampleName --param1=param1Value --param2=param2Value’
e.g.,
Running a a ProSe example with command line parameters and specify (existent) output directory:
./ns3 run ‘exampleName --param1=param1Value --param2=param2Value’ --cwd=‘outputDirectory’
e.g.,
NR ProSe example’s source code location:
src/nr/examples/nr-prose-examples/

## Slide 9: NR ProSe direct discovery

## Slide 10: NR ProSe direct discovery: Overview
5G ProSe direct discovery allows 5G ProSe-enabled UEs discover other 5G ProSe-enabled UEs within their reach using direct NR radio transmissions. It can be performed independently from 5G ProSe Direct Communication or can be used to initiate one-to-one unicast communication.
Direct discovery can be either open or restricted depending on whether an explicit permission from the 5G ProSe-enabled UE being discovered is needed.
UE 1
UE 3
UE 4
(out of reach)
UE 2
SL
SL
UE 5
(not authorized to perform 5G NR Discovery)

## Slide 11: NR ProSe direct discovery: Models
Model A is a discovery announcement using a broadcast of a single discovery message and can be either open or restricted.
The UE sending the ProSe PC5 discovery message is called the “announcing UE” and the “monitoring UE” is the UE that triggers the lower layer to start listening for such message.
Model B employs a set of discovery messages based on a Request/Response exchange and can only be restricted.
The UE sending the first discovery message is called the “Discoverer UE” and the UE receiving and responding to this message is called the “Discoveree UE”.
Model A
Model B
UE A (announcing)
UE B
(monitoring)
UE A (discoverer)
UE B
(discoveree)
Discovery Announcement
Discovery Solicitation
Discovery Response

## Slide 12: NR ProSe direct discovery: Interfaces
PC3a:
The reference point between the UE and the 5G Direct Discovery Name Management Function (5G DDNMF), which is the logical function managing inter-PLMN 5G ProSe Direct Discovery operations.
It is used to authorize 5G ProSe Direct Discovery request and perform allocation of ProSe Application Codes / ProSe Restricted Codes corresponding to ProSe Application Identities used for 5G ProSe Direct Discovery.
PC5:
The reference point between ProSe-enabled UEs used for control and user plane for 5G ProSe Direct Discovery, 5G ProSe Direct Communication and 5G ProSe UE-to-Network Relay.
UE A
UE B
PC5
PC3a
5GC
5G DDNMF

## Slide 13: NR ProSe direct discovery: PC5 Procedures
PC5 discovery supports the initiation and completion of the following PC5 procedures for both models A and B:
Direct or peer discovery (for open and restricted modes)
  to enable a ProSe-enabled UE to detect and identify another ProSe-enabled UE over PC5 interface.
Group member discovery (only available for restricted mode) both public safety use and commercial services
  to enable a ProSe-enabled UE to detect and identify another ProSe-enabled UE that belongs to the same application layer group (e.g. sharing the same application layer group ID) over PC5 interface.
UE-to-Network relay discovery (only available for restricted mode)
  to enable a ProSe-enabled UE to detect and identify another ProSe-enabled UE over PC5 interface for UE-to-Network relay communication between a UE and 5G Core (5GC).
Discovery
PDCP
RLC
MAC
PHY
Discovery
PDCP
RLC
MAC
PHY
UE A
UE B
PC5

## Slide 14: NR ProSe direct discovery: Implementation
PC3a discovery is not supported
UEs are considered pre-authorized to perform PC5 discovery.
The required parameters (e.g., ProSe Application Code, Relay Service Code, filters, etc) are already provided in the scenario to use during the PC5 discovery process.
PC5 discovery is implemented
Peer and U2N relay discovery are implemented with both discovery models (Model A and Model B).
Group discovery is partially supported and be simulated using one Destination L2 ID for a group of UEs.
A discovery transmission periodicity is added, i.e., the discovery message is sent periodically based on discovery interval that can be set in the scenario (default value is equal to 1 second).

## Slide 15: NR ProSe direct discovery: Implementation
Two discovery models:
Model A for broadcast announcements
Model B for request/response exchange
Structure to store discovery information:
Discovery model
Discovery role
The application code
The Layer 2 ID of the target destination
The UE can play multiple roles depending the discovery model used and on which side (transmitting or receiving) it is.

## Slide 16: NR ProSe direct discovery: Peer Discovery
These functions from the NrSlProseHelper can be called in the scenario when performing peer discovery, allowing the start and the end of the discovery process and taking into consideration discovery parameters (e.g., ProSe Application Code, Destination L2 ID, and the role played by the UE).

## Slide 17: NR ProSe direct discovery: Peer Discovery - Example
Each UE is announcing its own service.
All UEs are monitoring other UEs’ services.
Model A is used and the role each UE plays in the discovery process is specified in the scenario. If instead of Announcing/Monitoring, Discoverer/Discoveree was used, then Model B is considered.
nr-prose-discovery.cc
Source code: src/nr/examples/nr-prose-examples/nr-prose-discovery.cc

## Slide 18: NR ProSe direct discovery: Peer Discovery - Example
Successful
mutual discovery:
Both UEs were able to discover each other.
UE 1 succeeded to discover UE 2, while UE 2 was not able to discover UE 1
The NrSlDiscoveryTrace.txt trace file is generated automatically when discovery is performed.
As specified in the example, Model A is used, and the discovery is performed every 2 seconds (default value in the example) until the end of the simulation (10 seconds).
nr-prose-discovery.cc
Running the scenario:
Simulation output files:

## Slide 19: NR ProSe direct discovery: Relay Discovery
These functions from the NrSlProseHelper can be called in the scenario when performing relay discovery, allowing the start and the end of the relay discovery process and taking into consideration discovery parameters (e.g., Relay Service Code, Destination L2 ID, discovery model, and the role played by the UE).

## Slide 20: NR ProSe direct discovery: Relay Discovery - Example
2 UEs are placed within reach from each other and performing relay discovery.
To establish the relay discovery, we:
  define the pre-requisite parameters: the Relay Service Code and the Layer-2 ID of the target destination.
  schedule the start of the discovery process and specify the Relay Service Code, the destination L2 ID, the used discovery model (Model B here), and the role for each UE (relay/remote here).
The Relay Service code, the destination L2 ID, and the discovery model should be all configured the same for both UEs. And the discovery roles should align with the discovery procedure considered.
nr-prose-discovery-l3-relay.cc
Source code: src/nr/examples/nr-prose-examples/nr-prose-discovery-l3-relay.cc

## Slide 21: NR ProSe direct discovery: Relay Discovery - Example
Successful relay discovery
Failed relay discovery due to propagation loss
Model B is used, and the discovery is performed every 2 seconds (which is the default value in the example) until the end of the simulation (10 seconds).
nr-prose-discovery-l3-relay.cc
Running the scenario:
Simulation output files:

## Slide 22: NR ProSe direct discovery: Relay Discovery - Example
Changing the discovery periodicity to 4 seconds changes the output results.
nr-prose-discovery-l3-relay.cc
Simulation output files:
Running the scenario with a different discovery interval:

## Slide 23: NR ProSe unicast communication

## Slide 24: NR ProSe unicast communication - Overview
NR SL Unicast
  Logical link between two UEs
  Local control at different layers
How the link is established, used and controlled is defined by the service using it
  NR V2X communication over PC-5, Unicast mode communication over PC5 reference point (TS 23.287 - 5.2.1.4)
  Unicast Mode 5G ProSe direct communications, One-to-one 5G ProSe direct communications ( TS 24.554 – 7.2)
Summary from TS 38.300 NR; NR and NG-RAN Overall description; Stage-2- Section 16.9 Sidelink |  |  | 
Functionality | Unicast | Groupcast | Broadcast
Transmission and reception of user traffic over the Sidelink | Between two peer UEs | Between UEs belonging to a group | Between UEs
Transmission and reception of control information over the Sidelink | Between peer UEs (PC5-S, PC5-RRC) | - | -
Support of sidelink HARQ feedback | Yes | Yes | -
Support of sidelink transmit power control | Yes | - | -
Support of RLC AM | Yes | - | -
Support of one PC5-RRC connection | Between peer UEs | - | -
Detection of radio link failure for the PC5-RRC connection. | Yes | - | -
UE 2
UE 1
SL

## Slide 25: NR ProSe unicast communication - Overview
Desired configurations
  Manual unicast link association from scenario (pre-simulation)
    Enables the evaluation of unicast communication protocols
      Scheduling, HARQ, power control
      Link control (PC5-S, PC5-RRC, RLF)
  Dynamic unicast link association during simulation
    Enables the use of unicast communication in other functionalities
      E.g., U2N relay, U2U relay
        Link establishment after relay discovery and selection
U2N
Relay UE
Remote
UE
UE 2
UE 1
SL
SL
U2U
Relay UE
Source
UE
SL
Target
UE

## Slide 26: NR ProSe unicast communication - Implementation
Protocol (TS 24.554 section 7.2)
  5G ProSe direct link establishment procedure
  5G ProSe direct link modification procedure
  5G ProSe direct link identifier update procedure
  5G ProSe direct link keep-alive procedure
  5G ProSe direct link release procedure
  PC5 QoS flow establishment over 5G ProSe direct link
  PC5 QoS flow match over 5G ProSe direct link
  Data transmission over 5G ProSe direct link
  5G ProSe direct link security mode control procedure
  5G ProSe direct link re-keying procedure
  5G ProSe direct link authentication procedure
Architecture
  One direct link per pair of UEs
  A UE can have multiple direct links with different peer UEs
  Each UE keeps a direct link instance associated to the peer L2ID in the link

## Slide 27: NR ProSe unicast communication - Example
nr-prose-unicast-multi-link.cc
Direct link configuration:
UE 0
Node ID: 0
L2ID: 1
IPv4 addr: 7.0.0.2
UE 1
Node ID: 1
L2ID: 2
IPv4 addr: 7.0.0.3
UE 2
Node ID: 2
L2ID: 3
IPv4 addr: 7.0.0.4
Source code: src/nr/examples/nr-prose-examples/nr-prose-unicast-multi-link.cc
Three UEs deployed with a configurable inter-UE distance (default 20 m)
Each pair of UEs establish a unicast direct link with each other at a configurable simulation time (default 2 s)
The initiating UE is selected by increased node ID, i.e.,
20 m
20 m
Link | Initiating UE | Target UE
UE0 <--> UE1 | UE0 | UE1
UE0 <--> UE2 | UE0 | UE2
UE1 <--> UE2 | UE1 | UE2

## Slide 28: NR ProSe unicast communication - Example
UE 0
Node ID: 0
L2ID: 1
IPv4 addr: 7.0.0.2
UE 1
Node ID: 1
L2ID: 2
IPv4 addr: 7.0.0.3
UE 2
Node ID: 2
L2ID: 3
IPv4 addr: 7.0.0.4
Traffic configuration:
nr-prose-unicast-multi-link.cc
Source code: src/nr/examples/nr-prose-examples/nr-prose-unicast-multi-link.cc
A CBR traffic flow from the initiating UE towards the target UE is configured by default
The packet size, data rate and general starting time of the flows can be configured. The default values:
Actual starting time is randomized within a 100 ms range to avoid simultaneous transmissions
CBR: Constant Bit Rate
Parameter | Default value
udpPacketSize | 200 Bytes
dataRate | 16 kb/s
startTrafficTime | 3 s

## Slide 29: NR ProSe unicast communication - Example
Simulation standard output:
Running the scenario:
Simulation output files:
UE 0
Node ID: 0
L2ID: 1
IPv4 addr: 7.0.0.2
UE 1
Node ID: 1
L2ID: 2
IPv4 addr: 7.0.0.3
UE 2
Node ID: 2
L2ID: 3
IPv4 addr: 7.0.0.4
nr-prose-unicast-multi-link.cc

## Slide 30: NR ProSe unicast communication - Example
Simulation output files:
UE 0
Node ID: 0
L2ID: 1
IPv4 addr: 7.0.0.2
UE 1
Node ID: 1
L2ID: 2
IPv4 addr: 7.0.0.3
UE 2
Node ID: 2
L2ID: 3
IPv4 addr: 7.0.0.4
nr-prose-unicast-multi-link.cc

## Slide 31: NR ProSe unicast communication - Example
UE 0
Node ID: 0
L2ID: 1
IPv4 addr: 7.0.0.2
UE 1
Node ID: 1
L2ID: 2
IPv4 addr: 7.0.0.3
UE 2
Node ID: 2
L2ID: 3
IPv4 addr: 7.0.0.4
nr-prose-unicast-multi-link.cc
Simulation output files:

## Slide 32: NR ProSe unicast communication - Example
Simulation output files:
DB Browser for SQLite (Windows/Linux/MacOS) available in: https://sqlitebrowser.org/dl/
nr-prose-unicast-multi-link.cc

## Slide 33: NR ProSe unicast communication - Example
UE 0
Node ID: 0
L2ID: 1
IPv4 addr: 7.0.0.2
UE 1
Node ID: 1
L2ID: 2
IPv4 addr: 7.0.0.3
UE 2
Node ID: 2
L2ID: 3
IPv4 addr: 7.0.0.4
nr-prose-unicast-multi-link.cc
Running the scenario with bidirectional traffic:
Simulation
standard
output
When the parameter ‘bidirectional’ is set to true, additional CBR flows are added from the target UE towards the initiating UE of each link
Simulation output files:

## Slide 34: NR ProSe L3 UE-to-Network relay

## Slide 35: NR ProSe L3 UE-to-Network relay - Overview
U2N
Relay UE
Remote
UE 2
SL
Remote
UE 1
SL
UL
DL
App
Server
PC5
Uu
N3
N6
APP
PDU layer
SDAP
PDCP
RLC
MAC
PHY
PDU Relay | 
SDAP | SDAP
PDCP | PDCP
RLC | RLC
MAC | MAC
PHY | PHY
Remote UE
U2N Relay UE
SDAP | GTP-U
PDCP | UDP IP
RLC | 
MAC | L2
PHY | L1
PDU layer
GTP-U
UDP IP
L2
L1
NG-RAN
Relay UE’s
UPF
Layer 3
Architecture
APP
APP
PDU layer
SDAP
PDCP
RLC
MAC
PHY
 | Adaptation
RLC | RLC
MAC | MAC
PHY | PHY
SDAP | GTP-U
PDCP | UDP IP
Adaptation | 
RLC | 
MAC | L2
PHY | L1
PDU layer
GTP-U
UDP IP
L2
L1
Remote UE’s
UPF
Remote UE
U2N Relay UE
NG-RAN
Layer 2
Architecture
PC5
Uu
N3
N6
APP
GTP-U: GPRS Tunneling Protocol
IP: Internet Protocol
L1: Layer 1
L2: Layer 2
MAC: Media Access Control
PDU: Protocol Data Unit
PDCP: Packet Data Convergence Protocol
PHY: Physical Layer
RLC: Radio Link Control
SDAP: Service Data Adaptation Protocol
UDP: User Datagram Protocol
Core Network
gNB
PC5
Uu
Ns-3 implementation
focus

## Slide 36: NR ProSe L3 UE-to-Network relay - Overview
Core Network
TS 23.304
U2N
Relay
UE
UL
DL
Remote
UE
SL
gNB

## Slide 37: NR ProSe L3 UE-to-Network relay - Overview
Core Network
TS 23.304
U2N
Relay
UE
UL
DL
Remote
UE
SL
4a. Standard procedure
4b. Configured from the scenario
5. Simplified: IP addresses are exchanged during step 4
6. Simple model: Remote UE switches from NW bearer to SL bearer with Relay UE – No QoS management
7. Ideal: Function call to the LTE PGW corresponding function
ns-3 model
gNB

## Slide 38: NR ProSe L3 UE-to-Network relay - Example
nr-prose-l3-relay.cc
Source code: src/nr/examples/nr-prose-examples/nr-prose-l3-relay.cc
UL
DL
SL
SL
UL
DL
UE1
Remote Host
UE2
UE3
UE4
Relay UE
Remote UEs
In-network
UE
gNB
Topology:
Spectrum division
The scenario uses one operational band, containing one component carrier, and two bandwidth parts (BWP):
BWP0 is used for in-network communication, i.e., UL and DL between in-network UEs and gNBs
BWP1 is used for direct communication, i.e., SL between the relay UE and the remote UEs
Relay UE uses both BWPs
Some special config is needed to do SL only in BWP1
Remote UEs configure both BWPs but SL only uses BWP1

## Slide 39: NR ProSe L3 UE-to-Network relay - Example
UL
DL
SL
SL
UL
DL
UE1
Node ID: 1
IPv4 addr: 7.0.0.2
Remote Host
Node ID: 9
IPv4 addr: 1.0.0.2
UE2
Node ID: 2
L2ID: 2
IPv4 addr: 7.0.0.3
UE3
Node ID: 3
L2ID: 3
IPv4 addr: 7.0.0.4
UE4
Node ID: 4
L2ID: 4
IPv4 addr: 7.0.0.5
Relay UE
Remote UEs
In-network
UE
gNB
Source code: src/nr/examples/nr-prose-examples/nr-prose-l3-relay.cc
Network connections:
nr-prose-l3-relay.cc
ProSe layer configuration:

## Slide 40: NR ProSe L3 UE-to-Network relay - Example
UL
DL
SL
SL
UL
DL
UE1
Node ID: 1
IPv4 addr: 7.0.0.2
Remote Host
Node ID: 9
IPv4 addr: 1.0.0.2
UE2
Node ID: 2
L2ID: 2
IPv4 addr: 7.0.0.3
UE3
Node ID: 3
L2ID: 3
IPv4 addr: 7.0.0.4
UE4
Node ID: 4
L2ID: 4
IPv4 addr: 7.0.0.5
Relay UE
Remote UEs
In-network
UE
gNB
Source code: src/nr/examples/nr-prose-examples/nr-prose-l3-relay.cc
L3 U2N Relay configuration (1/2)
nr-prose-l3-relay.cc
Activates radio bearer to be used for relaying traffic
Gets bearer Id and stores it in the corresponding context in the ProSe layer (used to direct relayed packets)
Sets EpcHelper in the ProSe layer (used to configure data path in the network when a Remote UE connects)

## Slide 41: NR ProSe L3 UE-to-Network relay - Example
UL
DL
SL
SL
UL
DL
UE1
Node ID: 1
IPv4 addr: 7.0.0.2
Remote Host
Node ID: 9
IPv4 addr: 1.0.0.2
UE2
Node ID: 2
L2ID: 2
IPv4 addr: 7.0.0.3
UE3
Node ID: 3
L2ID: 3
IPv4 addr: 7.0.0.4
UE4
Node ID: 4
L2ID: 4
IPv4 addr: 7.0.0.5
Relay UE
Remote UEs
In-network
UE
gNB
Source code: src/nr/examples/nr-prose-examples/nr-prose-l3-relay.cc
L3 U2N Relay configuration (2/2)
nr-prose-l3-relay.cc
Assign IDs
Schedules the creation of the corresponding direct link instances in both UEs participating in the U2N relay connection (Remote UE is the initiating UE of the direct link and relay UE is the target UE)

## Slide 42: NR ProSe L3 UE-to-Network relay - Example
UL
DL
SL
SL
UL
DL
UE1
Node ID: 1
IPv4 addr: 7.0.0.2
Remote Host
Node ID: 9
IPv4 addr: 1.0.0.2
UE2
Node ID: 2
L2ID: 2
IPv4 addr: 7.0.0.3
UE3
Node ID: 3
L2ID: 3
IPv4 addr: 7.0.0.4
UE4
Node ID: 4
L2ID: 4
IPv4 addr: 7.0.0.5
Relay UE
Remote UEs
In-network
UE
gNB
Source code: src/nr/examples/nr-prose-examples/nr-prose-l3-relay.cc
Traffic configuration
nr-prose-l3-relay.cc
CBR traffic with configured packet size and data rate
One traffic flow from each UE to the Remote Host
One traffic flow from the Remote Host to each UE
Remote UEs code examples:

## Slide 43: NR ProSe L3 UE-to-Network relay - Example
UL
DL
SL
SL
UL
DL
UE1
Node ID: 1
IPv4 addr: 7.0.0.2
Remote Host
Node ID: 9
IPv4 addr: 1.0.0.2
UE2
Node ID: 2
L2ID: 2
IPv4 addr: 7.0.0.3
UE3
Node ID: 3
L2ID: 3
IPv4 addr: 7.0.0.4
UE4
Node ID: 4
L2ID: 4
IPv4 addr: 7.0.0.5
Relay UE
Remote UEs
In-network
UE
gNB
Source code: src/nr/examples/nr-prose-examples/nr-prose-l3-relay.cc
Bearer activation
nr-prose-l3-relay.cc
A dedicated EPS bearer is activated in each UE for each traffic flow direction
For the remote UEs, these bearers won’t be used, but the information on them is used to configure the traffic redirection on the NAS layer once a remote UEs connects to a relay UE.

## Slide 44: NR ProSe L3 UE-to-Network relay - Example
UL
DL
SL
SL
UL
DL
UE1
Node ID: 1
IPv4 addr: 7.0.0.2
Remote Host
Node ID: 9
IPv4 addr: 1.0.0.2
UE2
Node ID: 2
L2ID: 2
IPv4 addr: 7.0.0.3
UE3
Node ID: 3
L2ID: 3
IPv4 addr: 7.0.0.4
UE4
Node ID: 4
L2ID: 4
IPv4 addr: 7.0.0.5
Relay UE
Remote UEs
In-network
UE
gNB
nr-prose-l3-relay.cc
Simulation standard output:
Running the scenario:
1
2
4
3

## Slide 45: NR ProSe L3 UE-to-Network relay - Example
UL
DL
SL
SL
UL
DL
UE1
Node ID: 1
IPv4 addr: 7.0.0.2
Remote Host
Node ID: 9
IPv4 addr: 1.0.0.2
UE2
Node ID: 2
L2ID: 2
IPv4 addr: 7.0.0.3
UE3
Node ID: 3
L2ID: 3
IPv4 addr: 7.0.0.4
UE4
Node ID: 4
L2ID: 4
IPv4 addr: 7.0.0.5
Relay UE
Remote UEs
In-network
UE
gNB
nr-prose-l3-relay.cc
Simulation output files (1/2):

## Slide 46: NR ProSe L3 UE-to-Network relay - Example
nr-prose-l3-relay.cc
Simulation output files (2/2):

## Slide 47: L3 U2N Relay selection (Integration direct discovery with L3 U2N relay)

## Slide 48: NR ProSe relay selection: Overview
The 5G ProSe remote UE triggers the relay selection procedure if is authorized to act as a remote UE towards a UE-to-network (U2N) relay UE and already obtained a list of UE-to-network relay UE candidate(s) fulfilling ProSe layer criteria and other lower layers criteria.
A Reselection is triggered if:
  the previously selected relay is no longer available; or
  the relay configuration parameters have been updated and the relay no longer fulfil the selection requirements; or
  the remote received a PROSE DIRECT LINK ESTABLISHMENT REJECT message or a PROSE DIRECT LINK RELEASE REQUEST from the relay; or
  No response is obtained after the transmission of multiple PROSE DIRECT LINK ESTABLISHMENT REQUEST or PROSE DIRECT LINK KEEPALIVE REQUEST messages.

## Slide 49: NR ProSe relay selection: Implementation
Relay (re)selection is triggered if:
  A new U2N relay UE is discovered
  A new RSRP measurement is received
Three relay selection algorithms are implemented:
  FirstAvailableRelay: selecting the first available U2N relay UE in the list of discovered relays.
  RandomRelay: selecting a U2N relay UE randomly from the list of discovered relays.
  MaxRsrpRelay (3GPP-compliant): selecting the U2N relay UE that has the best RSRP measurement after fulfilling the threshold and hysteresis criteria.
Relay (re)selection calls for:
  The release of the direct link with the current U2N relay UE
  The establishment of the direct link with the newly selected U2N relay UE
  The bearers’ reconfiguration by removing the old ones used for the released relay UE (this would be triggered by the RELEASE procedure) and adding new ones with the selected U2N relay (this would be triggered by the ESTABLISHMENT procedure).
Remote UE
PROSE DIRECT LINK RELEASE REQUEST
Old Relay UE
PROSE DIRECT LINK RELEASE ACCEPT
New Relay UE
PROSE DIRECT LINK ESTABLISHMENT REQUEST
PROSE DIRECT LINK ESTABLISHMENT ACCEPT
Timer T5087
Timer T5080

## Slide 50: NR ProSe relay selection: Example
Topology:
  This example is composed of one gNB and 3 UEs: The first 2 UEs act as in-network L3 UE-to-Network relay UEs (which are attached to the gNB). The third UE acts as out-of-network remote UE.
  All UEs are randomly deployed and follow a random walk mobility model.
  The UEs will start performing NR discovery at random simulation times.
  The relay selection algorithm can be selected in the scenario.
Traffic:
  Uplink and downlink traffic (of the same configuration) is flowing between the remote UE and the server.
Trace outputs:
  NrSlPc5SignallingPacketTrace.txt: log of the transmitted and received PC5 signaling messages used for the establishment and/or release of each ProSe unicast direct link.
  NrSlRelayNasRxPacketTrace.txt: log of the packets received and routed by the NAS of the UE acting as L3 UE-to-Network UE.
  NrSlRelayDiscoveryTrace.txt: to keep track of discovered relays.
  NrSlRelaySelectionTrace.txt: to keep track of relay selection attempts.
nr-prose-discovery-l3-relay-selection.cc
Source code: src/nr/examples/nr-prose-examples/nr-prose-discovery-l3-relay-selection.cc

## Slide 51: NR ProSe relay selection: Example
To be called in the scenario:
nr-prose-discovery-l3-relay-selection.cc
Source code: src/nr/examples/nr-prose-examples/nr-prose-discovery-l3-relay-selection.cc

## Slide 52: NR ProSe relay selection: Example
Traffic is relayed through relay UE 1 to remote UE 3
Traffic is relayed through relay UE 2 to remote UE 3
nr-prose-discovery-l3-relay-selection.cc
Simulation standard output
Running the scenario:
Simulation output files:

## Slide 53: NR ProSe relay selection: Example
nr-prose-discovery-l3-relay-selection.cc
Relevant simulation output files:
First time selecting a relay UE after a successful discovery
A relay selection may be triggered by the discovery of an eligible relay or the reception of an RSRP measurement corresponding to a discovery procedure.
Once a new relay UE is randomly selected, a release procedure is triggered with the previously selected relay and an establishment procedure is started for the newly selected relay.
Already connected to the same relay

## Slide 54: NR ProSe relay selection: Example
nr-prose-discovery-l3-relay-selection.cc
Running the scenario with a different relay selection algorithm:
Simulation standard output:
Simulation output files:
Traffic is relayed through relay UE 1 (7.0.0.2)
Traffic is relayed through relay UE 2 (7.0.0.3)

## Slide 55: NR ProSe relay selection: Example
nr-prose-discovery-l3-relay-selection.cc
Relevant simulation output files:
First time selecting a relay UE (Relay L2ID 1) after a successful discovery
Relay L2ID 2 shows a better RSRP measurement, relay reselection is triggered: release of the connection with Relay L2ID 1 and establishment of the connection with the Relay L2ID 2
Relay L2ID 1 has a better RSRP measurement again, relay reselection is triggered
* Already connected to the best relay
Relay L2ID 2 has a better RSRP measurement again, relay reselection is triggered
*
*
*

## Slide 56: NR ProSe relay selection: Example
Visualization with NetSimulyzer

## Slide 57: Future work
Near term:
  Integrate the recent updates made to the NR Sidelink Sensing, Scheduling, and HARQ feedback models to the NR ProSe module.
  Complete the release of the NR ProSe code.
Long term:
  Implement the 3GPP Rel-18 one-hop NR ProSe UE-to-UE (U2U) relay functionality.
  Investigate and prototype multi-hop NR ProSe U2U relay functionality and how to incorporate it into the 5G NR infrastructure.

## Slide 58
aziza.benmosbah@nist.gov
samantha.gamboaquintiliani@nist.gov
https://www.nist.gov/programs-projects/public-safety-communications