## Slide 1
ns-3 training
Slides (and all ns-3 documentation) are provided by the authors
under Creative Commons CC-BY-SA-4.0
  https://creativecommons.org/licenses/by-sa/4.0/

## Slide 2: Agenda
What is ns-3?
Software overview, capabilities, and build system
ns-3 core (simulation time, events, random variables)
ns-3 network (Nodes, Packets, NetDevices)
Other key modules (mobility, propagation)
ns-3 TCP/IP and applications
ns-3 training
ns-3 cttc-nr-demo (5G NR)

## Slide 3
Nodes, Applications, NetDevices
Most simulations involve packet exchanges such as depicted below
Application
Application
Protocol
stack
Node
NetDevice
NetDevice
Application
Application
Protocol
stack
Node
NetDevice
NetDevice
Sockets-like
API
Channel
Channel
Packet(s)‏

## Slide 4: ns-3 Packet
Packet is an advanced data structure with the following capabilities
  Supports fragmentation and reassembly
  Supports real or virtual application data
  Extensible
  Serializable (for emulation)
  Supports pretty-printing
  Efficient (copy-on-write semantics)

## Slide 5: ns-3 Packet structure
Analogous to an Linux or BSD mbuf/skbuff

## Slide 6: Copy-on-write
Copy data bytes only as needed
Figure source: Mathieu Lacage's Ph.D. thesis

## Slide 7: Headers and trailers
Most operations on packet involve adding and removing an ns3::Header
class ns3::Header must implement four methods:
Serialize()
Deserialize()
GetSerializedSize()
Print()

## Slide 8: Headers and trailers (cont.)
Headers are serialized into the packet byte buffer with Packet::AddHeader() and removed with Packet::RemoveHeader()
Headers can also be 'Peeked' without removal
Ptr<Packet> pkt = Create<Packet> ();
UdpHeader hdr; // Note: not heap allocated
pkt->AddHeader (hdr);
Ipv4Header iphdr;
pkt->AddHeader (iphdr);

## Slide 9: Packet tags
Packet tag objects allow packets to carry around simulator-specific metadata
  Such as a "unique ID" for packets or cross-layer info
Tags may associate with byte ranges of data, or with the whole packet
  Distinction is important when packets are fragmented and reassembled
Tags presently are not preserved across serialization boundaries (e.g. MPI)

## Slide 10: PacketTag vs. ByteTag
Two tag types are available: PacketTag and ByteTag
  ByteTags run with bytes
  PacketTags run with packets
When Packet is fragmented, both copies of Packet get copies of PacketTags
When two Packets are merged, only the PacketTags of the first are preserved
PacketTags may be removed individually; ByteTags may be removed all at once

## Slide 11: Tag example
Here is a simple example illustrating the use of tags from the code in src/internet/model/udp-socket-impl.cc:
  Ptr<Packet> p; // pointer to a pre-existing packet
  SocketIpTtlTag tag
  tag.SetTtl(m_ipMulticastTtl); // Convey the TTL from UDP layer to IP layer
  p->AddPacketTag(tag);
This tag is read at the IP layer, then stripped (src/internet/model/ipv4-l3-protocol.cc):
  uint8_t ttl = m_defaultTtl;
  SocketIpTtlTag tag;
  bool found = packet->RemovePacketTag(tag);
  if (found)
  {
  ttl = tag.GetTtl();
  }

## Slide 12: Packet metadata
Packets may optionally carry metadata
  record every operation on a packet's buffer
  implementation of Packet::Print for pretty-printing of the packet
  sanity check that when a Header is removed, the Header was actually present to begin with
Not enabled by default, for performance reasons
To enable, insert one or both statements:
  Packet::EnablePrinting ();
  Packet::EnableChecking ();

## Slide 13: Ptr<Packet>
Packets are reference counted objects that support the smart pointer class Ptr
Use a templated "Create" method instead of CreateObject for ns3::Objects
Typical creation:
  Ptr<Packet> pkt = Create<Packet> ();
In model code, Packet pointers may be const or non-const; often Packet::Copy() is used to obtain non-const from const
  Ptr<const Packet> cpkt = ...;
  Ptr<Packet> p = cpkt->Copy ();

## Slide 14: Queues in ns-3
Queues are objects for storing packets
A templated Queue class exists to support a few use cases
  simple queues such as a DropTail
  WifiMacQueue
  a Linux-like QueueDisc class
Dequeue
Enqueue
Common operations: GetNBytes (); GetNPackets (); etc.

## Slide 15: Linux-like TC architecture in ns-3
Figure source: Stefano Avallone (2017 training)

## Slide 16
Simulation setup
We have already explained the operation of the start of the program (configuring default values and command line arguments)
int
main (int argc, char *argv[])
{
DataRate dataRate = DataRate ("100Mbps");
...
CommandLine cmd;
cmd.AddValue("distance","the distance between the two nodes",distance);
...
cmd.Parse (argc, argv);

## Slide 17
Nodes and ns-3 Objects
The next statements create the scenario, usually starting with the Node objects:
Ptr<Node> senderNode = CreateObject<Node> ();
Ptr<Node> receiverNode = CreateObject<Node> ();
NodeContainer nodes;
nodes.Add (senderNode);
nodes.Add (receiverNode);
What is CreateObject<Node> ()?
What is a NodeContainer?

## Slide 18
class ns3::Object
ns-3 is, at heart, a C++ object system
ns-3 objects that inherit from base class ns3::Object get several additional features beyond a standard C++ class
  smart-pointer memory management (Class Ptr)
  dynamic run-time object aggregation
  type metadata
  an attribute system
Instead of:
Node* senderNode = new Node;
in ns-3, we write
Ptr<Node> senderNode = CreateObject<Node> ();
Create a smart pointer to hold objects of type Node, similar to C++ std::shared_ptr
Create a new Node object on the heap

## Slide 19: Object aggregation
Figure source: Walid Younes

## Slide 20
ns-3 attributes
Attributes are special member variables that the Object system exposes in a way to facilitate configuration
An Attribute can be connected to an underlying variable or function
  e.g. TcpSocket::m_cwnd;
  or a trace source

## Slide 21: Attribute configuration
Attributes can be configured using Object::SetAttribute(); e.g.:
  idealBeamformingHelper->SetAttribute("BeamformingMethod", TypeIdValue(DirectPathBeamforming::GetTypeId()));
Attributes can be configured using Config::SetDefault(); e.g.:
  Config::SetDefault("ns3::LteRlcUm::MaxTxBufferSize", UintegerValue(999999999));
Many ns-3 configuration helpers expose methods to configure attributes

## Slide 22: Object TypeIds
TypeId is metadata associated to the object, defining:
  A unique string identifying the class.
  The base class of the subclass, within the metadata system.
  The set of accessible constructors in the subclass.
  A list of publicly accessible properties ("attributes") of the class.
TypeIds are commonly referred to by string (e.g., "ns3::Node")
The TypeId of any object can be queried from its Ptr
  std::cout << p->GetTypeId().GetName() << std::endl;
If you have a base class pointer, you can generally learn the subclass of the object that it is pointing to

## Slide 23
Helper API
The ns-3 “helper API” provides a set of classes and methods that make common operations easier than using the low-level API
Consists of:
  container objects
  helper classes
The helper API is implemented using the low-level API
Each function applies a single operation on a ''set of same objects”
  A typical operation is "Install()"

## Slide 24
Containers
Containers are part of the ns-3 “helper API”
Containers group similar objects, for convenience
  They are often implemented using C++ std containers
Container objects also are intended to provide more basic (typical) API

## Slide 25
Helper API examples
NodeContainer: vector of Ptr<Node>
NetDeviceContainer: vector of Ptr<NetDevice>
InternetStackHelper
WifiHelper
MobilityHelper
OlsrHelper
... many ns-3 models provide a helper class

## Slide 26
Installation onto containers
Installing models into containers, and handling containers, is a key API theme
NodeContainer c;
c.Create (numNodes);
...
mobility.Install (c);
...
internet.Install (c);
...

## Slide 27: Helper differences
Most ns-3 Helper objects are not derived from ns3::Object
  They are normal C++ classes
The exception is LTE and NR module
  These helpers typically derive from ns3::Object, so are created using CreateObject<>, have attributes, etc.

## Slide 28
Mobility and position
Cartesian coordinate system
Nodes typically have a
MobilityModel with a
(time-varying) Position
Initial positions are
often allocated by
a PositionAllocator
This is a
NetAnim
screenshot

## Slide 29
Mobility and position
ns-3 position is represented on a 3D Cartesian (x,y,z) coordinate system
The MobilityHelper combines a mobility model and position allocator.
Position Allocators setup initial position of nodes (only used when simulation starts):
  List: allocate positions from a deterministic list specified by the user;
  Grid: allocate positions on a rectangular 2D grid (row first or column first);
  Random position allocators: allocate random positions within a selected form (rectangle, circle, …).
Mobility models specify how nodes will move during the simulation:
  Constant: position, velocity or acceleration;
  Waypoint: specify the location for a given time (time-position pairs);
  Trace-file based: parse files and convert into ns-3 mobility events, support mobility tools such as SUMO, BonnMotion (using NS2 format) , TraNS

## Slide 30
Propagation
Propagation module defines:
  Propagation loss models: Calculate the Rx signal power considering the Tx signal power and the respective Rx and Tx antennas positions.
  Propagation delay models: Calculate the time for signals to travel from the TX antennas to RX antennas.
Propagation delay models almost always set to:
  ConstantSpeedPropagationDelayModel: In this model, the signal travels with constant speed (defaulting to speed of light in vacuum)

## Slide 31
Propagation (cont.)
Propagation loss models:
  Many propagation loss models are implemented:
    Abstract propagation loss models: FixedRss, Range, Random, Matrix, …
    Deterministic path loss models: Friis, LogDistance, ThreeLogDistance, TwoRayGround, …
    Stochastic fading models: Nakagami, Jakes, …

## Slide 32
Propagation (cont.)
  A propagation loss model can be “chained” to another one, making a list. The final Rx power takes into account all the chained models. Example: path loss model + shadowing model + fading model
Figure source: Unknown

## Slide 33
Error models convert SNR to PER
Example error model curves used in the Wi-Fi module

## Slide 34
SpectrumChannel illustration
Figure source: ns-3 Model Library documentation