## Slide 1: IEEE 802.11 PSM in ns-3: A Novel Implementation and Evaluation under Channel Congestion
Shyam Krishnan Venkateswaran, Ching-Lun Tai, Yoav Ben-Yehezkel, Yaron Alpert , and Raghupathy Sivakumar
Georgia Institute of Technology, Texas Instruments
Workshop on ns-3 (WNS3) – June 22, 2022

## Slide 2: Towards Ultra-dense Networks
Local Area Networks are becoming denser by the day
Over 28 Billion Internet connected devices are expected by end of 2023 [1]

## Slide 3: Towards Ultra-dense Networks
Local Area Networks are becoming denser by the day
Over 28 Billion Internet connected devices are expected by end of 2023 [1]
  Smart doorbells
  TVs and Streaming devices
  Personal Computers
  Smart Phones and tablets
  Smart thermostats
  Soil moisture sensors
Periodic and sparse reporting IoT devices constitute a prominent use case

## Slide 4: Wi-Fi as an IoT Solution
Wi-Fi is
Wi-Fi supports low power operation allowing battery-operated client devices to enter Sleep states
Power Save Mechanism (PSM) allows power saving up to 99% for connectivity maintenance[2]
Newer Wi-Fi standards have provisions designed specifically for IoT
  Ubiquitous
  Standardized
Chart: 
| Peak Data Rate | Delay | Range | Mobility | Bandwidth | Number of Users | Cost | Spectrum Efficiency
WiFi | 1 | 0.1 | 0.1 | 0.02 | 1 | 0.000255 | 0.002 | 0.66667
  Customizable with tradeoffs
  Low-power operation friendly
TI CC3235
Silabs RS9116
Wi-Fi is becoming an increasingly suitable choice for mid-range low-power IoT

## Slide 5: Key Contributions
An open-source model for PSM that integrates with the Wi-Fi module in ns-3 that handles uplink (UL) and downlink (DL) unicast and multicast traffic
Using a comprehensive power model, a detailed evaluation of power performance of PSM in congested network scenarios
Insight into the impact of bidirectional nature of TCP traffic on power consumption in the presence of network congestion

## Slide 6: PSM – A Primer
Power Saving (PS) stations (STA) set the Power Management (PM) bit in UL data frames to 1
AP buffers packets for power saving stations at least till next relevant beacon
Buffer status for PS stations are indicated through the Traffic Indication Map (TIM) element in beacons
Stations can retrieve buffered unicast packets by polling the AP (PS-POLL)
AP delivers buffered multicast packets after every Delivery TIM (DTIM) beacon
t
Rx
Beacon
Tx PS-POLL
Tx
Rx
Legend
SLEEP
Packet for PS STA received at AP
Beacon
Rx
Rx PS-POLL
Tx Buffered Pkt
Rx Packet
Tx ACK
Rx ACK
AID in TIM
More data = 0
No buffered packets

## Slide 7: PSM Model – Related Work
PSM has been an area of active research owing to the exponential increase in low power devices
Ref. [3] and [4] use a PSM model in ns-2 – which is no longer maintained
Many works such as [5], [6], [7] implement models within custom simulators in C++ or MATLAB for evaluation
Ref. [8] uses a PSM model in ns-3 but is not open source
An open-source model for PSM in ns-3 is necessary for reproducibility and standardized evaluation

## Slide 8: PSM Model in ns-3
Major changes:
AP and STA MAC models are modified
New MAC queues at STA and AP to buffer packets
AP buffers packets for all PS STAs
STA MAC utilizes the ‘SLEEP’ PHY state
PS STAs receive all beacons
Traffic Indication Map (TIM) element is implemented and added to beacons
  TIM element format
  State Diagram for PSM implementation

## Slide 9: Power Modeling
Model is calibrated to a State-of-Art low power IoT chip (TI CC3235)
Power model recognizes traffic type and accounts for state transitions
TCP uplink – Estimated Power Consumption
Power Model - Calibration

## Slide 10: Simulation Setup
PS STA (STAPS) sends one TCP UL packet to TCP server every second
Other STAs offer constant bit rate (CBR) UL UDP traffic
Total offered load (load%) is measured as
Awake Time() is the percentage of time that STAPS is not in SLEEP state
  Simulation setup for nSTA=10

## Slide 11: TCP Power Performance with High Load
For TCP UL traffic, as network load increases from 0% to 100% with ,
increases from 1.58 mA to 3.29 mA - a 108% increase
increases from 1.28% to 4.52% - a 254% increase
Power consumption increases with increased total network load

## Slide 12: Effect of Bidirectional Traffic Flow
As network load increases from 0% to 100% with ,
increases by 53% for TCP traffic and by 28% for UDP traffic
increases by 187% for TCP traffic and by 112% for UDP traffic
Bidirectional nature of TCP traffic compounds the effect of network congestion on PSM power performance

## Slide 13: Summary and Future Work
We develop and validate an open-source model for PSM in ns-3
With sparse TCP UL traffic, a station using PSM can stay awake for up to 254% longer with 20 contending stations consuming over 108% more current
Bidirectional flow of TCP traffic increases the power consumption with PSM as network congestion increases – over 75% more time awake with 10 contending stations
For future work, we plan to model, evaluate, and optimize Target Wake Time (Wi-Fi 6) as a scheduling solution in tandem with Wi-Fi power save methods for low power operation

## Slide 14: Thank you

## Slide 15: References
[1] Cisco 2020: Cisco Annual Internet Report (2018–2023) White Paper.
[2] Venkateswaran, Shyam Krishnan, et al. "Extending Battery Life for Wi-Fi-Based IoT Devices: Modeling, Strategies, and Algorithm." Proceedings of the 19th ACM International Symposium on Mobility Management and Wireless Access. 2021.
[3] Ronny Krashinsky and Hari Balakrishnan. 2002. Minimizing Energy for Wireless Web Access with Bounded Slowdown. In Proceedings of the 8th annual international conference on Mobile computing and networking. 119–130.
[4] Xijian Chen, Yi Xie, and Chengyan Wang. 2011. Implementation and Analysis of IEEE 802.11 PSM in ns-2. In 2011 International Conference on Machine Learning and Cybernetics, Vol. 3. 1250–1255.
[5] Jung-Ryun Lee and Dong-Ho Cho. 2006. An Energy-efficient Downlink Multiple Access Control Considering Congestion in Wireless LANs.
[6] Yi Li, Xin Zhang, and Kwan L. Yeung. 2015. A Novel Delayed Wakeup Scheme for Efficient Power Management in Infrastructure-based IEEE 802.11 WLANs. In 2015 IEEE Wireless Communications and Networking Conference (WCNC)
[7] Yu Zhang, Mingfei Wei, Chen Cheng, Xianjin Xia, Tao Gu, Zhigang Li, and Shining Li. 2017. Exploiting Delay-aware Load Balance for Scalable 802.11 PSM in Crowd Event Environments. Wireless Communications and Mobile Computing 2017
[8] Prawit Chumchu. 2015. An Extension to IEEE 802.11 Power Save Mode for ns-3. In 2015 Seventh International Conference on Ubiquitous and Future Networks. 799–804