## Slide 1: EESM-log-SGN: State-of-the-art PHY Layer Abstraction for Complex Network Simulation
Sian Jin, Thomas R. Henderson
A Hands-On Tutorial
2021 WNS-3 Workshop
ACK: Sumit Roy, Sebastien Deronne, Jun Hyeon Park
NSF ICE-T 1836725

## Slide 2: Prior to talk
Prerequisite:
  MATLAB 2020b or later version
  MATLAB WLAN Toolbox 2020b or later version
  MATLAB Parallel Computing Toolbox 2020b or later version (optional)
Matlab Code: https://github.com/sianjin/EESM-log-SGN
ns-3 code: https://gitlab.com/sderonne/ns-3-11be/-/tree/log_sgn_ofdma_mu_mimo_phy_abstraction

## Slide 3: Outline
Motivations for efficient PHY layer abstraction
Principles of EESM-log-SGN
Implementation guide of EESM-log-SGN
Demo of MATLAB offline link simulation steps (main part of this tutorial)
Demo of ns-3 online network simulation steps

## Slide 4: What is PHY layer abstraction?
PHY layer abstraction represents packet error rate (PER) as a function of
Subcarriers allocation
Channel type
RX SNR
MIMO dimension
MCS
RX INR
Full PHY simulation block diagram

## Slide 5: What is PHY layer abstraction?
PHY layer abstraction represents packet error rate (PER) as a function of
Subcarriers allocation
Channel type
RX SNR
MIMO dimension
MCS
RX INR
Full PHY simulation block diagram

## Slide 6: What is PHY layer abstraction?
PHY layer abstraction represents packet error rate (PER) as a function of
Subcarriers allocation
Channel type
RX SNR
MIMO dimension
MCS
RX INR
Full PHY simulation block diagram

## Slide 7: What is PHY layer abstraction?
PHY layer abstraction represents packet error rate (PER) as a function of
Subcarriers allocation
Channel type
RX SNR
MIMO dimension
MCS
RX INR
Full PHY simulation block diagram

## Slide 8: What is PHY layer abstraction?
PHY layer abstraction represents packet error rate (PER) as a function of
Subcarriers allocation
Channel type
RX SNR
MIMO dimension
MCS
RX INR
Full PHY simulation block diagram

## Slide 9: What is PHY layer abstraction?
PHY layer abstraction represents packet error rate (PER) as a function of
Subcarriers allocation
Channel type
RX SNR
MIMO dimension
MCS
RX INR
Full PHY simulation block diagram

## Slide 10: What is PHY layer abstraction?
PHY layer abstraction represents packet error rate (PER) as a function of
Subcarriers allocation
Channel type
RX SNR
MIMO dimension
MCS
Packet error or success
Compare
RX INR
Full PHY simulation block diagram

## Slide 11: What is PHY layer abstraction?
WifiPhy
MacLow
MAC layer
SendPacket
Success/fail
ns-3 WifiNetDevice example
PHY entity
getReceptionStatus
PHY layer
Interference helper
Error model
PER
getReceptionStatus
Configuration parameters
Success/fail
Success/fail

## Slide 12: Issues with PHY layer abstractions
Exploding Complexity
Increasing MIMO dimensions
Complex channels
Greater co-channel interference (denser networks)
Higher order of MU transmissions

## Slide 13: PHY layer complexity: runtimes
Increasing MIMO dimensions
Complex channels
Greater interference (denser network)
Higher order of MU transmissions
Single link, 40,000 packets, targeting [10-2, 1] avg PER

## Slide 14: PHY layer complexity: runtimes
Very large runtime for running full PHY simulation (end-to-end encoding/decoding modulation/demodulating steps)
Increasing MIMO dimensions
Complex channels
Greater interference (denser network)
Higher order of MU transmissions
Single link, 40,000 packets, targeting [10-2, 1] avg PER

## Slide 15: PHY layer complexity: runtimes
Very large runtime for running full PHY simulation (end-to-end encoding/decoding modulation/demodulating steps)
Need improved PHY layer abstractions: preserve simulation accuracy while reducing run-times
Increasing MIMO dimensions
Complex channels
Greater interference (denser network)
Higher order of MU transmissions
Single link, 40,000 packets, targeting [10-2, 1] avg PER

## Slide 16: History of ns-3 PHY layer abstractions
802.11a PHY layer abstraction - YANS model (2006) [1]
  OFDM, SISO, IID AWGN channel
  Based on analytical bounds to obtain PER
[1] Mathieu Lacage and Thomas R. Henderson. 2006. Yet another network simulator. Proc. 2006 workshop on ns-2: the IP network simulator (WNS2 '06)

## Slide 17: History of ns-3 PHY layer abstractions
802.11n PHY layer abstraction - link-to-system (L2S) mapping (2017) [2]
  OFDM, SISO, IID frequency-selective channel
  Based on link simulations results and lookup tables to obtain PER
  Require channel generation in ns-3; slow
[2] Rohan Patidar, Sumit Roy, Thomas R. Henderson, and Amrutha Chandramohan. 2017. Link-to-System Mapping for ns-3 Wi-Fi OFDM Error Models. Proc. of Workshop on ns-3 (WNS3 '17).

## Slide 18: History of ns-3 PHY layer abstractions
Modeling complex WiFi PHY - EESM-log-SGN (2020-2021) [3,4]
  OFDM/OFDMA MIMO/MU-MIMO, IID frequency-selective channel, interference
  Based on link simulations results and lookup tables to obtain PER
  Does not require channel generation in ns-3; fast
[3] Sian Jin, Sumit Roy, Weihua Jiang, and Thomas R. Henderson. 2020. Efficient Abstractions for Implementing TGn Channel and OFDM-MIMO Links in ns-3. WNS3 2020. ACM, New York, NY, USA, 33–40.
[4] Sian Jin, Sumit Roy, and Thomas R. Henderson. 2021. Efficient PHY Layer Abstraction for Fast Simulations in Complex System Environments. IEEE TCOM. Early access.

## Slide 19: Outline
Motivations for efficient PHY layer abstraction
Principles of EESM-log-SGN
Implementation guide of EESM-log-SGN
Demo of MATLAB offline link simulation steps (main part of this tutorial)
Demo of ns-3 online network simulation steps

## Slide 20: PHY layer assumptions
Channel model: independent and identically distributed (IID) frequency-selective fading channel
IID over time: each packet in the simulation experiences an indep. channel realization
Channel instance is invariant during the transmission of each packet (block fading)
Time
Channel gain
Packet
Packet
Packet
Packet
[4] Sian Jin, Sumit Roy, and Thomas R. Henderson. 2021. Efficient PHY Layer Abstraction for Fast Simulations in Complex System Environments. IEEE TCOM. Early access.

## Slide 21: Traditional PHY layer abstraction [5]
L2S mapping suggested by IEEE TGax group:
for i-th subcarrier and j-th stream
[5] IEEE TGax Group, “IEEE p802.11 Wireless Lans: 11ax Evaluation Methodology,” 2016.

## Slide 22: Traditional PHY layer abstraction [5]
Over an OFDM/OFDMA MIMO/MU-MIMO system, abstracting the post-MIMO processing SINRs over all subcarriers and spatial streams into a a single scalar metric - effective SINR
The single effective SINR is a convenient metric to describe the packet-level performance for a network simulator
L2S mapping function

## Slide 23: Traditional PHY layer abstraction [5]
Over an OFDM/OFDMA MIMO/MU-MIMO system, abstracting the post-MIMO processing SINRs over all subcarriers and spatial streams into a a single scalar metric - effective SINR
The single effective SINR is a convenient metric to describe the packet-level performance for a network simulator
2 popular L2S mapping functions: EESM and RBIR
L2S mapping function

## Slide 24: Traditional PHY layer abstraction [5]
Over an OFDM/OFDMA MIMO/MU-MIMO system, abstracting the post-MIMO processing SINRs over all subcarriers and spatial streams into a a single scalar metric - effective SINR
The single effective SINR is a convenient metric to describe the packet-level performance for a network simulator
2 popular L2S mapping functions: EESM and RBIR
For EESM, and
L2S mapping function

## Slide 25: Traditional PHY layer abstraction
Runtime
Runtime reduces; but still large & increases with MIMO dimension, MU dimension, # of interferers
Single link, 40,000 packets, targeting [10-2, 1] avg PER

## Slide 26: Key Observation
Observation: upper layer only needs instantaneous PER
L2S mapping suggested by IEEE TGax group:

## Slide 27: Key Observation
Observation: upper layer only needs instantaneous PER
Q1: Can we bypass runtime-expensive matrix calculation and directly store average PER (mean of instantaneous PER)?
L2S mapping suggested by IEEE TGax group:

## Slide 28: Key Observation
Observation: upper layer only needs instantaneous PER
Q1: Can we bypass runtime-expensive matrix calculation and directly store average PER (mean of instantaneous PER)?
L2S mapping suggested by IEEE TGax group:
No variance, skewness, kurtosis, time correlation information

## Slide 29: Key Observation
Observation: upper layer only needs instantaneous PER
L2S mapping suggested by IEEE TGax group:
Q2: Can we bypass runtime-expensive matrix calculation and directly model instantaneous PER?

## Slide 30: Key Observation
Observation: upper layer only needs instantaneous PER
L2S mapping suggested by IEEE TGax group:
Q2: Can we bypass runtime-expensive matrix calculation and directly model instantaneous PER?
Cannot provide models of instantaneous PERs for different packet lengths

## Slide 31: Key Observation
Observation: upper layer only needs instantaneous PER
L2S mapping suggested by IEEE TGax group:
Q3: Can we bypass runtime-expensive matrix calculation and directly model effective SNR?

## Slide 32: Key Observation
Observation: upper layer only needs instantaneous PER
L2S mapping suggested by IEEE TGax group:
Q3: Can we bypass runtime-expensive matrix calculation and directly model effective SNR?
Effective SNR is insensitive to packet length and is easy to be mapped into instantaneous PER

## Slide 33: New Method: EESM-log-SGN
L2S mapping:
Assume IID channel, model effective SNR distribution, and directly outputs IID effective SINRs
Time
Effective SNR
Packet
Packet
Packet
Packet

## Slide 34: New Method: EESM-log-SGN
L2S mapping:
Log-skew generalized normal (log-SGN) distribution
Under IID channel & EESM L2S mapping function, effective SNR distribution follows:

## Slide 35: New Method: EESM-log-SGN
L2S mapping:
Log-skew generalized normal (log-SGN) distribution
Under IID channel & EESM L2S mapping function, effective SNR distribution follows:
PDF of X

## Slide 36: New Method: EESM-log-SGN
L2S mapping:
Log-skew generalized normal (log-SGN) distribution
Under IID channel & EESM L2S mapping function, effective SNR distribution follows:
PDF of X

## Slide 37: New Method: EESM-log-SGN
log-SGN distribution

## Slide 38: New Method: EESM-log-SGN
log-SGN distribution

## Slide 39: New Method: EESM-log-SGN
log-SGN distribution
log-SGN parameters depend on: OFDM/OFDMA MIMO/MU-MIMO, bandwidth, MCS, channel types, SNR and INR

## Slide 40: New Method: EESM-log-SGN
Runtime of the proposed method is significantly smaller and insensitive to system dim change!
Single link, 40,000 packets, targeting [10-2, 1] avg PER

## Slide 41: Outline
Motivations for efficient PHY layer abstraction
Principles of EESM-log-SGN
Implementation guide of EESM-log-SGN
Demo of MATLAB offline link simulation steps (main part of this tutorial)
Demo of ns-3 online network simulation steps

## Slide 42: General implementation flow

## Slide 43
Full PHY simulation
Packet error or success
Compare
Compute packet error states

## Slide 44: Full PHY Simulation
Compute post-MIMO processing SINR
i.e., SINR on different subcarriers and streams

## Slide 45: # of Packets per Full PHY Simulation
For achieving average PER at , running n packets per simulation
can achieve PER estimation accuracy bound
For example, for achieving average PER down to 0.01, it’s recommended to run n=40000 packets per simulation

## Slide 46
EESM tuning parameter optimization
Overview

## Slide 47
EESM tuning parameter optimization
Objective:
Algorithm

## Slide 48
EESM tuning parameter optimization
Post-MIMO processing SINR
Effective SINR
Packet error states
Objective:
Satisfied
Algorithm

## Slide 49
EESM tuning parameter optimization
Post-MIMO processing SINR
Effective SINR
Packet error states
Objective:
Satisfied
Not satisfied
Update
Algorithm

## Slide 50: Effective SINR histogram generation

## Slide 51: Effective SINR histogram generation
Effective SINR formula:

## Slide 52: Effective SINR histogram generation
Effective SINR formula:

## Slide 53: Log-SGN parameters optimization

## Slide 54: Log-SGN parameters optimization

## Slide 55: Log-SGN parameters optimization

## Slide 56: EESM-log-SGN PHY layer abstraction

## Slide 57: EESM-log-SGN PHY layer abstraction

## Slide 58: Outline
Motivations for efficient PHY layer abstraction
Principles of EESM-log-SGN
Implementation guide of EESM-log-SGN
Demo of MATLAB offline link simulation steps (main part of this tutorial)
Demo of ns-3 online network simulation steps

## Slide 59: MATLAB link simulation
Matlab Code: https://github.com/sianjin/EESM-log-SGN
Link simulation flow:

## Slide 60: PHY configuration 1
Communication system: IEEE 802.11ax
  Coding and modulation: LDPC at MCS 4
OFDM with 242 subcarriers
1×1 SISO with 1 stream
Channel type: TGax channel model-D
RX SNR = TX SNR - path loss (dB)
Interference-free case
Simulate 4000 packets
Full PHY simulation

## Slide 61: 11ax subcarrier allocation
[5] MathWorks, “802.11ax Parameterization for Waveform Generation and Simulation,” 2020. web: https://www.mathworks.com/help//wlan/ug/802-11ax-parameterization-for-waveform-generation-and-simulation.html.
Full PHY simulation

## Slide 62: PHY configuration 1
Communication system: IEEE 802.11ax
  Coding and modulation: LDPC at MCS 4
242-tone OFDM (allocation idx 192)
1×1 SISO with 1 stream
Channel type: TGax channel model-D
RX SNR = [11,15,19,23] dB (set in getBox0SimParams.m)
Interference-free case
Packet length = 1000 byte
Simulate 4000 packets
Open: MU code basic/1 Full PHY (no interferer)/fullPHY.m
Full PHY simulation

## Slide 63: PHY configuration 1
Outputs of full PHY simulation:
  “sinrPer_Config192_Model-D_1-by-1_MCS4.mat”
  4000 {post-MIMO processing SINR matrix, packet error state} pairs for each RX SNR
A figure on the right
  Full PHY and RBIR prediction
  2 curves match -> full PHY simulation is a success
Open: MU code basic/1 Full PHY (no interferer)/fullPHY.m
Full PHY simulation

## Slide 64: PHY configuration 1
Copy “sinrPer_Config192_Model-D_1-by-1_MCS4.mat” generated in Step 1 into MU code basic/2 EESM parameter optimization
EESM tuning parameter optimization

## Slide 65: PHY configuration 1
EESM tuning parameter optimization
Open: MU code basic/2 EESM parameter optimization/eesmAbstractionPerVsEffSinr.m
Load: “sinrPer_Config192_Model-D_1-by-1_MCS4.mat”
  Select initial EESM tuning parameter beta according to the MCS
  Run eesmAbstractionPerVsEffSinr.m to optimize beta value

## Slide 66: PHY configuration 1
EESM tuning parameter optimization
Open: MU code basic/2 EESM parameter optimization/eesmAbstractionPerVsEffSinr.m
Outputs of EESM tuning parameter optimization:
  “eesmEffSinr_Config192_Model-D_1-by-1_MCS4.mat”
  Optimized EESM tuning parameter (beta)
A figure on the right showing:

## Slide 67: PHY configuration 1
Copy:
“sinrPer_Config192_Model-D_1-by-1_MCS4.mat” generated in Step 1 & “eesmEffSinr_Config192_Model-D_1-by-1_MCS4.mat” generated in Step 2
into MU code basic/ 3 Basic EESM-log-SGN method
EESM tuning parameter optimization

## Slide 68: PHY configuration 1
Log-SGN parameters optimization
Open: MU code basic/3 Basic EESM-log-SGN method/eesmLogSGNBasic.m
  Load: “sinrPer_Config192_Model-D_1-by-1_MCS4.mat” & “eesmEffSinr_Config192_Model-D_1-by-1_MCS4.mat”
Choose the RX SNR snrs(snrIdx) that we want to simulate
  Choose snrIdx = 1 in this example
  Run eesmLogSGNBasic.m to obtain effective SINR histogram and statistically fit the histogram into the log-SGN distribution

## Slide 69: PHY configuration 1
Log-SGN parameters optimization
Open: MU code basic/3 Basic EESM-log-SGN method/eesmLogSGNBasic.m
Outputs of log-SGN parameters optimization:
  snr_LogSGNParam_Config192_Model-D_1-by-1_MCS4.mat
  Can be converted into snr_LogSGNParam_Config192_Model-D_1-by-1_MCS4.txt in ns-3 format via logSGNmat2txt.m
A figure on the right
  Effective SINR histogram under traditional L2S mapping
  Optimized log-SGN distribution by EESM-log-SGN method

## Slide 70: PHY configuration 2
Communication system: IEEE 802.11ax
  Coding and modulation: LDPC at MCS 5
OFDM with 242 subcarriers
1×1 SISO with 1 stream
Channel type: TGax channel model-B
RX SNR = TX SNR - path loss (dB)
Interference-free case
Simulate 4000 packets
Full PHY simulation

## Slide 71: PHY configuration 2
Communication system: IEEE 802.11ax
  Coding and modulation: LDPC at MCS 5
242-tone OFDM (allocation idx 192)
1×1 SISO with 1 stream
Channel type: TGax channel model-B
RX SNR = [14,21,25,28] dB (set in getBox0SimParams.m)
Interference-free case
Packet length = 1000 byte
Simulate 4000 packets
Open: MU code basic/1 Full PHY (no interferer)/fullPHY.m
Full PHY simulation

## Slide 72: PHY configuration 2
Outputs of full PHY simulation:
  “sinrPer_Config192_Model-B_1-by-1_MCS5.mat”
  4000 {post-MIMO processing SINR matrix, packet error state} pairs for each RX SNR
A figure on the right
  Full PHY and RBIR prediction
  2 curves match -> full PHY simulation is a success
Open: MU code basic/1 Full PHY (no interferer)/fullPHY.m
Full PHY simulation

## Slide 73: PHY configuration 2
Copy “sinrPer_Config192_Model-B_1-by-1_MCS5.mat” generated in Step 1 into MU code basic/2 EESM parameter optimization
EESM tuning parameter optimization

## Slide 74: PHY configuration 2
EESM tuning parameter optimization
Open: MU code basic/2 EESM parameter optimization/eesmAbstractionPerVsEffSinr.m
Load: “sinrPer_Config192_Model-B_1-by-1_MCS5.mat”
  Select initial EESM tuning parameter beta according to the MCS
  Run eesmAbstractionPerVsEffSinr.m to optimize beta value

## Slide 75: PHY configuration 2
EESM tuning parameter optimization
Open: MU code basic/2 EESM parameter optimization/eesmAbstractionPerVsEffSinr.m
Outputs of EESM tuning parameter optimization:
  “eesmEffSinr_Config192_Model-B_1-by-1_MCS5.mat”
  Optimized EESM tuning parameter (beta)
A figure on the right showing:

## Slide 76: PHY configuration 2
Copy:
“sinrPer_Config192_Model-B_1-by-1_MCS5.mat” generated in Step 1 & “eesmEffSinr_Config192_Model-B_1-by-1_MCS5.mat” generated in Step 2
into MU code basic/ 3 Basic EESM-log-SGN method
EESM tuning parameter optimization

## Slide 77: PHY configuration 2
Log-SGN parameters optimization
Open: MU code basic/3 Basic EESM-log-SGN method/eesmLogSGNBasic.m
  Load: “sinrPer_Config192_Model-B_1-by-1_MCS5.mat” & “eesmEffSinr_Config192_Model-B_1-by-1_MCS5.mat”
Choose the RX SNR snrs(snrIdx) that we want to simulate
  Run eesmLogSGNBasic.m to obtain effective SINR histogram and statistically fit the histogram into the log-SGN distribution

## Slide 78: PHY configuration 2
Log-SGN parameters optimization
Open: MU code basic/3 Basic EESM-log-SGN method/eesmLogSGNBasic.m
Outputs of log-SGN parameters optimization:
  snr_LogSGNParam_Config192_Model-B_1-by-1_MCS5.mat
  Can be converted into snr_LogSGNParam_Config192_Model-B_1-by-1_MCS5.txt in ns-3 format via logSGNmat2txt.m
A figure on the right
  Effective SINR histogram under traditional L2S mapping
  Optimized log-SGN distribution by EESM-log-SGN method

## Slide 79: Outline for the following presentation
Motivations for efficient PHY layer abstraction
Principles of EESM-log-SGN
Implementation guide of EESM-log-SGN
Demo of MATLAB offline link simulation steps (main part of this tutorial)
Demo of ns-3 online network simulation steps

## Slide 80: Backup slides

## Slide 81: History of ns-3 Error Models
YANS model
  Original ns-3 Wi-Fi PHY is based on OFDM, SISO, frequency-flat additive white Gaussian noise (AWGN) channel, and can be easily computed
  However, frequently-selective fading channels commonly occur in OFDM system, and this greatly impacts system performance

## Slide 82: History of ns-3 Error Models
Link-to-system (L2S) mapping
  A traditional abstraction for OFDM MIMO based PHY over a frequency-selective channel
  Block diagram suggested by IEEE TGax group:

## Slide 83: Backup slides
Simulation steps to implement L2S suggested by IEEE TGax group

## Slide 84: Full PHY simulation and PHY configuration
Fading channels to multiple users
Bits
FEC encoding
Stream parser
MIMO pre-coding
IDFT
IDFT
IDFT
MCS
Nss streams
Ntx TX chains
Interference
TX
RX
RX INR
RX SNR
DFT
DFT
MIMO de-coding
Reverse stream parser
FEC decoding
Bits
# of interference
Nrx RX chains
Subcarriers allocation
Channel type

## Slide 85: PHY configuration example
Communication system: IEEE 802.11ax
  Coding and modulation: LDPC at MCS 4
OFDMA allocation with 52 subcarriers
8×2 MIMO with 2 streams
Channel type: TGax channel model-D
  Widely used in IEEE 802.11 system evaluation
  Include frequency selectivity & antenna correlation
  Speed of the scatters/users: 0.089km/h (small Doppler)
  Inter-carrier interference (ICI) can be ignored
  Coherence time = 0.978s >> packet transmission time (~ hundred us), slow fading
RX SNR = TX SNR - path loss (dB)

## Slide 86: History of ns-3 PHY layer abstractions
Modeling complex WiFi PHY - EESM-log-SGN (2020-2021) [3,4]
  OFDM/OFDMA, MIMO/MU-MIMO, IID frequency-selective channel, inter-user interference
  Based on link simulations results and lookup tables to obtain PER
  Does not require channel generation in ns-3; fast
Extension to more realistic WiFi channel - EESM-log-AR (2021) [5]
  OFDM, MIMO, time-varying frequency-selective channel
[3] Sian Jin, Sumit Roy, Weihua Jiang, and Thomas R. Henderson. 2020. Efficient Abstractions for Implementing TGn Channel and OFDM-MIMO Links in ns-3. WNS3 2020. ACM, New York, NY, USA, 33–40.
[4] Sian Jin, Sumit Roy, and Thomas R. Henderson. 2021. Efficient PHY Layer Abstraction for Fast Simulations in Complex System Environments. IEEE TCOM. Early access.
[5] Sian Jin, Sumit Roy, and Thomas R. Henderson. 2021. EESM-log-AR: An Efficient Error Model for OFDM MIMO Systems over Time-Varying Channels. Accepted in WNS3 2021.

## Slide 87: EESM-log-SGN
Runtime
Runtime of EESM-log-SGN:
Small & insensitive to the change of MIMO dimension, MU dimension, # of interferers
* The runtime here is the recurring cost in network simulation. Before running these network simulations, the non-recurring (performed once per configuration) offline full PHY simulation cost on page 5 is still needed to obtain the parameters for network simulation.

## Slide 88: Storage-complexity aspects
Handling wide range of RX SNRs and INRs: challenge & principle
Fact: effective SNR/INR depends on RX SNR/INR
Challenge: cannot store effective SNR/INR
distribution under any RX SNR/INR
Solution: interpolate effective SNR/INR for
any RX SNR/INR using a small # of stored
effective SNR distributions - mixture model
Stored distributions
Estimated distribution

## Slide 89: Storage-complexity aspects
Handling numerous interference setups: challenge & principle
Effective SNR : the effective SINR under the interference-free scenario with a certain RX SNR
Effective INR : the effective SINR with signal from an interferer v only and with a certain RX INR
Solution: estimate effective SINR from effective SNR & effective INR - low storage complexity (LSC) solution
Effective SNR
Effective INR
Estimated effective SINR
|V|: # of interferers

## Slide 90: Storage-complexity aspects
Handling numerous interference setups: accuracy and runtime

## Slide 91: Average PER under of all proposed schemes
106 subcarriers, 8 × {2, 2} MU-MIMO with 2 streams/user, TGax channel model-D, MCS4,
the RX INR is 30dB lower than RX SNR

## Slide 92: Conclusion
Under IID slow fading channel model, EESM-log-SGN models effective SINR distribution directly
EESM-log-SGN achieves good accuracy in modeling the PHY performance, while the runtime is insensitive to system dimensionality change and is small
Storage challenges for a wide RX SNR/INR range - effectively solved
Time
Channel gain/effective SINR
Packet
Packet
Packet
Packet

## Slide 93: Multi-path Propagation

## Slide 94: Fading
Received signal power VS. distance

## Slide 95: Frequency-selective Channel
Frequency flat
Frequency selective
LOS
multi-path NLOS
LOS +

## Slide 96: Time-varying Channel

## Slide 97: TGax Channel Models
TGax channel Models: A~F
Power Vs received multi-path signal delay

## Slide 98: Jakes’ Model
Doppler spectrum
Uniform scattering environment